## Slide 1: Instrumental techniques for the study of swallowing

## Slide 2
Choice of a certain technique depends on the patient’s:
age
language
Cognition
medical diagnosis

## Slide 3: Types of swallowing studies
Imaging Procedures
Nonimaging Procedures

## Slide 4: Imagining procedures
These include:
Ultrasound
Scintigraphy
Videoendoscopy (FEES)
Vidieofluoroscopy

## Slide 5: ultrasound
It examines
      tongue function
      oral transit time
      Motion of the hyoid bone
Disadvantage:
inability to visualize the pharynx, because of the mix of tissue (cartilage, bone and muscle)
Which stage of swallowing does it allow us to study ?

## Slide 6: Scintigraphy
It is a nuclear medicine test. The patient swallows radioactive materials, swallows are imaged and recorded using a gamma camera
It examines
    Esophagus for existence of Gastroesophageal reflux disease.
    Amount of aspiration and residue
Disadvantage:
    radioactive material!!
    The physiology of the mouth and pharynx is not visualized

## Slide 7: Video-endoscopy
Videoendoscopy (FEES): Flexible fiberoptic examination of swallowing
It examines –
    oral cavity and pharynx from above
    Larynx pre-post swallowing (Blue Die)
    good for testing swallow/breath manuevers
Disadvantages:
    inability to visualize the oral stage, the swallow trigger, swallow physiology
    If Rigid scope is used, it will interfere with normal swallow,

## Slide 8: Vidieofluoroscopy
Videofluoroscopy/ Cinefluoroscopy: radiographic recording of anatomical structures in motion.
It Examines:
    the transfer of bolus through the oral cavity
    Pharynx
    Esophagus
Cinefluroscopy Disadvantages:
    radiation exposure
    Time for film development
    Choosing appropriate frame rate (8 frames/sec.?)

## Slide 9: Vidieofluoroscopy
Videofluoroscopy involves less radiation exposure, ability for frame to frame analysis, more information on bolus transit time, detection of motility problems, detection of the amount and etiology of aspiration.
Examines:
    oral activity during chewing and the oral stage of swallowing
    triggering the pharyngeal swallow in relation to the position of the bolus
    motor aspects of the pharyngeal swallow; movements of larynx, hyoid, tongue base pharyngeal wall, and cricopharyngeal movements

## Slide 10: Vidieofluoroscopy
Swallow physiology is detected and recorded for further examination in slow motion (pharyngeal swallow transit times = 1 to 2 seconds
Videofluoroscopy Disadvantages: - No measurement of pressures generated during swallowing…(why is it important?)

## Slide 11: Who Dose What?
SLPs usually assess and modify the oral and the pharyngeal stage
• MDs diagnose and treat the esophageal stage
• SLPs, in cooperation with radiologists conduct a Modified Barium Study (MBS): mixing Barium Sulpahte (contrast material) with the three food consistencies (liquids, puree food, & solid food): 1,2,5, and 10 ml swallows

## Slide 12: What can slps do
1. Postural techniques (e.g. chin tuck, head rotated to the affected side, etc.)
2. Improving Oral Sensory Awareness (sour bolus, larger bolus, thermal-tactile stimulation)
3. Swallow Maneuvers : Mendelsohn Maneuver (increasing lx closure duration), effortful swallow, etc.)
4. Food Consistency (Diet Changes): using puree foods for reduced laryngeal closure).

## Slide 13: Nominating procedure
Provide NO pictures…but parameters such as pressure or electrical energy generated at specific locations.

## Slide 14: Electromyography
Electromyography (EMG): placing two electrodes on the muscle in question to measure electrical activity
it was found that type of bolus affects muscle activity duration
Two types:
    Surface electrode EMG (placed on the skin)
    Hooked-wire electrode EMGE (needles in muscles, e.g. superior pharyngeal constrictor activity)

## Slide 15: Electromyography
surface EMG serves as a biofeedback mechanism. HOW:
The patient can monitor the timing and amount of laryngeal elevation during swallowing and Swallow Maneuvers (Mandelson, Effortful swallow etc..)
• Hooked-wire EMG: compare electrical activity of some muscles during speech and swallowing…

## Slide 16: Electroglottography
Electroglottography (EGG): Tracks laryngeal impedance (VF movement ), laryngeal elevation, biofeedback for patients

## Slide 17: Cervical Auscultation
Cervical Auscultation: listening to and recording sounds of swallowing
•The “Click-Clunk” Approach 
•Using a microphone, we can listen to the click of opening the Eustachian tube (initiating the swallow) and the clunk of the esophagus opening (end of pharyngeal swallow)