## Slide 1: Digital Electronics and Computer Organization Lab ENCS 2110
Experiment No. 7 - Constructing Memory Circuits Using Flip−Flops

## Slide 2: Memory Types
1) Random Access Memory (RAM) is like a temporary workspace for your computer.
It's a type of memory that allows your computer to store and quickly access data that it needs to run programs and perform tasks.
Think of it as a desk where you can place things you're actively working on. The more RAM your computer has, the more tasks it can handle simultaneously and the faster it can switch between them.
However, keep in mind that RAM is temporary storage, and once you turn off your computer, the data in RAM is cleared.

## Slide 3: Memory Types
2) Read-Only Memory (ROM) is like a pre-written book for your computer.
It's a type of memory that stores information permanently, and unlike RAM, you can't easily change or write new data to it.
It contains essential instructions and data that your computer needs to start up and perform basic functions, like a set of rules the computer always follows. Even when you turn off your computer, the information in ROM remains intact.
It's called "read-only" because, in general, you can only read from it, not write to it like you can with RAM.

## Slide 4: CONSTRUCTING RANDOM ACCESS MEMORY (RAM) WITH D FLIP-FLOP
The following figure shows one bit memory made of D flip flop.
When CS=0, tri-state gates U1 and U2 do not operate, so data input is not possible, the flip- flop output Q is not sent to the I/O terminal. The memory is not chosen/disabled
When CS=1, W/R controls the D flip-flop. When W/R' =1, U1 opens but U2 does not, I/O will accept data input. If W/R'=0, the exact opposite will happen and I/O act as the data output.

## Slide 5: CONSTRUCTING RANDOM ACCESS MEMORY (RAM) WITH D FLIP-FLOP
Building 4-bit memory using 4 D flip flops.
It has 2 cells, each cell with 2 bits.
When CS1=1, RAM1 I/O1 and I/O2 are selected. Address line A is used to select between RAM1 and RAM2. Since there is only one address line, we can only select from 2 RAMs. each CS can only select a 2-bit RAM, so the total capacity is 2×2.

## Slide 6: Implementation of the two-bit memory

## Slide 7: Memory structure
Address
1bit
1bit
1bit
1bit
Each memory cell must have an address
In each cell, it can be divided into a number of bits, famous types are: 1 byte (8 bits) 2 bytes (16 bit) for each cell
How can we know the number of cells in the memory?
How can we calculate the memory entire size?
Cell 1
Cell 2
Cell 3
.
.
.
.
.
Cell n-1

## Slide 8: Memory in read mode
Address
1bit
1bit
1bit
1bit
In read mode, memory needs the following:
Data Bus
Address Bus
Memory Controller
Read Enable Signal
Enable signal
Data Output Buffer
Cell 1
Cell 2
Cell 3
.
.
.
.
.
Cell n-1

## Slide 9: Memory in read mode
Address
1bit
1bit
1bit
1bit
Data Bus: The data bus is the pathway through which data is transferred between the memory and other components of the computer, such as the CPU. In read mode, the data bus is used to transmit the data from the memory to the requesting component.
Cell 1
Cell 2
Cell 3
.
.
.
.
Cell n-1
Data bus

## Slide 10: Memory in read mode
Address
1bit
1bit
1bit
1bit
Address Bus: The address bus is responsible for carrying the memory address to locate the specific data that needs to be read. The size of the address bus determines the maximum addressable memory space.
Cell 1
Cell 2
Cell 3
.
.
.
.
Cell n-1
Data bus
Address bus

## Slide 11: Memory in read mode
Address
1bit
1bit
1bit
1bit
Memory Controller: The memory controller manages the communication between the CPU and the memory. It sends signals to the memory modules to read data from specific addresses and ensures that the data is properly transferred to the requesting component.
Cell 1
Cell 2
Cell 3
.
.
.
.
Cell n-1
Data bus
Address bus
Chip Select

## Slide 12: Memory in read mode
Address
1bit
1bit
1bit
1bit
Read Enable Signal: This signal indicates that the memory is in read mode and ready to provide data. It is often controlled by the memory controller.
Cell 1
Cell 2
Cell 3
.
.
.
.
Cell n-1
Data bus
Address bus
Chip Select
Read Signal

## Slide 13: Memory in read mode
Address
1bit
1bit
1bit
1bit
Enable Signal: When the memory is enabled, then it works as usual, while if it s disabled it does not work at all.
Cell 1
Cell 2
Cell 3
.
.
.
.
.
Cell n-1
Address bus
Chip Select
Read Signal

## Slide 14: Memory in write mode
Address
1bit
1bit
1bit
1bit
In write mode, memory needs the following:
Data Bus
Address Bus
Memory Controller
Write Enable Signal
Enable signal
Data Output Buffer
Cell 1
Cell 2
Cell 3
.
.
.
.
.
Cell n-1

## Slide 15: Memory in write mode
Address
1bit
1bit
1bit
1bit
Data Bus: The data bus is still important in write mode, as it is used to transmit the data from the component (usually the CPU) to the memory for storage.
Cell 1
Cell 2
Cell 3
.
.
.
.
.
Cell n-1
Data bus

## Slide 16: Memory in write mode
Address
1bit
1bit
1bit
1bit
Address Bus: The address bus is necessary to specify the location in the memory where the data should be written. The size of the address bus determines the maximum addressable memory space.
Cell 1
Cell 2
Cell 3
.
.
.
.
.
Cell n-1
Data bus
Address bus

## Slide 17: Memory in write mode
Address
1bit
1bit
1bit
1bit
Memory Controller: The memory controller manages the communication between the CPU and the memory. It sends signals to the memory modules to write data to specific addresses and ensures that the data is properly stored.
Cell 1
Cell 2
Cell 3
.
.
.
.
.
Cell n-1
Data bus
Address bus
Chip Select

## Slide 18: Memory in write mode
Address
1bit
1bit
1bit
1bit
Write Enable Signal: This signal indicates that the memory is in write mode and ready to accept data. It is controlled by the memory controller and is used to enable the memory cells for writing.
Cell 1
Cell 2
Cell 3
.
.
.
.
.
Cell n-1
Data bus
Address bus
Chip Select
Write Signal

## Slide 19: Memory in write mode
Address
1bit
1bit
1bit
1bit
Enable Signal: When the memory is enabled, then it works as usual, while if it s disabled it does not work at all
Cell 1
Cell 2
Cell 3
.
.
.
.
.
Cell n-1
Data bus
Address bus
Chip Select
Write Signal

## Slide 20: What does Random mean in RAM?
Imagine you have a bookshelf where each shelf is like a slot in RAM, and each book on a shelf is like a piece of data. Now, in a regular bookshelf (not a "random access" one), if you want the book on the fifth shelf, you have to start from the first shelf and go through them one by one until you reach the fifth. This takes time.
In a "random access" bookshelf (like RAM), you can instantly jump to the fifth shelf without going through the others. This ability to directly access any shelf is what makes it "random access“ which is much faster.
Address 0
Address 128
Address 200
1bit
1bit
1bit
1bit
Cell 1
Cell 2
Cell 3
.
.
.
.
.
Cell n-1

## Slide 21: What does Random mean in RAM?
In Random Access Memory (RAM), the concept of "random access" means that any memory cell can be accessed directly, irrespective of its physical location which means that addresses 0, 128 and 200 have the same access time. This is different from sequential access, where you'd have to go through data in order, like reading through a book.
Address 0
Address 128
Address 200
1bit
1bit
1bit
1bit
Cell 1
Cell 2
Cell 3
.
.
.
.
.
Cell n-1

## Slide 22: 64-BIT RANDOM ACCESS MEMORY (RAM) CIRCUIT
7489 IC is a RAM which was made to have 64 bit memory size.
Each cell has 4 bits.
The IC has 16 cells.
How to calculate total size?
How many address bits should it have?
How many data bits should it have?

## Slide 23: 64-BIT RANDOM ACCESS MEMORY (RAM) CIRCUIT
7489 IC is a RAM which was made to have 64 bit memory size.
Each cell has 4 bits.
The IC has 16 cells.
How to calculate total size?
Total size = 4 bits/cell X 16 cell = 64 bits.
How many address bits should it have?
How many data bits should it have?

## Slide 24: 64-BIT RANDOM ACCESS MEMORY (RAM) CIRCUIT
7489 IC is a RAM which was made to have 64 bit memory size.
Each cell has 4 bits.
The IC has 16 cells.
How to calculate total size?
Total size = 4 bits/cell X 16 cell = 64 bits
How many address bits should it have?
4 (log number of cells)
How many data bits should it have?

## Slide 25: 64-BIT RANDOM ACCESS MEMORY (RAM) CIRCUIT
7489 IC is a RAM which was made to have 64 bit memory size.
Each cell has 4 bits.
The IC has 16 cells.
How to calculate total size?
Total size = 4 bits/cell X 16 cell = 64 bits
How many address bits should it have?
4 (log number of cells)
How many data bits should it have?
4 (cell size of bits)

## Slide 26: 7489 IC modes

## Slide 27: Questions
If we want to build a 128 bit Ram using 7489 IC how many Ics do we need?
If we want to build a 256 bit Ram using 7489 IC how many Ics do we need?
How can we control the multiple ICs?

## Slide 29: Building 256 bit RAM from IC

## Slide 30
Why did we need 6 address bits here while before 4 bits were enough?

## Slide 31
Why did we need 6 address bits here while before 4 bits were enough?
We have 16 cells * 4 = 64 cell
Log64 = 6 bits

## Slide 32
Question: Save the number 5 At the address 200

## Slide 33
Question: Save the number 5 At the address 200
Data:
5 -> 0101
Address:
Memory 1 --> 0-63
Memory 2 --> 64-127
Memory 3 --> 128-191
Memory 4 --> 192-255 so, 200 is in the 4th memory
Quarter 4 has 16 cell, each has 4 bits --> Cell 1  192-195 Cell 2  196-199 Cell 3  200-203 so, 200 is in the 4th memory at the 3rd cell
A5A4 = 11  4th Memory A3A2A1A0 = 0010  3rd Cell

## Slide 34: Experiment No. 11 - Arithmetic Elements

## Slide 35: ALU
It consists of two major parts: the arithmetic unit and the logic unit. The output, either arithmetic or logic which is selected by the selection switches

## Slide 36: Pin assignments
How many inputs do you see?
How many outputs do you see?
How many control bits do you see?

## Slide 37: Pin assignments
The circuit has two 4-bit inputs A and B, as well as a “carry-in” (Cn) input.
There is a mode control input (M). M=1  Arithmetic , M=0  Logic
There are 4 function-select lines S0, S1, S2, S3 forming logic or arithmetic operations.
The mode control input (M) and function-select lines (S0~S3) determines which function it will perform.
It has a 4-bit output (F3~F0); a “carry-out” or “Cn+4” output.
The biggest advantage of the design is its ability to perform arithmetic functions such as addition, subtraction. multiplication; and logic functions such as AND, XOR functions.

## Slide 38: Selection line
When M=1:
S3S2S1S0=0000  Addition S3S2S1S0=0001  Subtraction . . . .
Note: Watch out for the value of Cn if you want to take previous carry into consideration Note: Watch out for Cn+4 if you want to take output carry into consideration

## Slide 39: Even/Odd parity

## Slide 40: Even bit parity generator