## Slide 1: IP Datagram format
ver
length
32 bits
payload data
(variable length,
typically a TCP
or UDP segment)
16-bit identifier
header
checksum
time to
live
source IP address
head.
len
type of
service
flgs
fragment
offset
upper
layer
destination IP address
options (if any)
IP protocol version number
header length(bytes)
upper layer protocol (e.g., TCP or UDP)
total datagram
length (bytes)
“type” of service:
diffserv (0:5)
ECN (6:7)
fragmentation/
reassembly
TTL: remaining max hops
(decremented at each router)
20 bytes of TCP
20 bytes of IP
= 40 bytes + app layer overhead for TCP+IP
overhead
e.g., timestamp, record route taken
32-bit source IP address
32-bit destination IP address
header checksum
Maximum length: 64K bytes
Typically: 1500 bytes or less

## Slide 2: IP fragmentation/reassembly
network links have MTU (max. transfer size) - largest possible link-level frame
  different link types, different MTUs
large IP datagram divided (“fragmented”) within net
  one datagram becomes several datagrams
  “reassembled” only at destination
  IP header bits used to identify, order related fragments
fragmentation:
in: one large datagram
out: 3 smaller datagrams
reassembly
…
…

## Slide 3: IP fragmentation/reassembly
ID
=x
offset
=0
fragflag
=0
length
=4000
ID
=x
offset
=0
fragflag
=1
length
=1500
ID
=x
offset
=185
fragflag
=1
length
=1500
ID
=x
offset
=370
fragflag
=0
length
=1040
one large datagram becomes
several smaller datagrams
example:
4000 byte datagram
MTU = 1500 bytes
1480 bytes in data field
offset =
1480/8

## Slide 4: IP addressing
Q: How does an ISP get block of addresses?
A: ICANN: Internet Corporation for Assigned
Names and Numbers
  allocates addresses
  manages DNS
  assigns domain names, resolves disputes

## Slide 5: IPv4
IPv4 uses four octets in a group to create an IP address and each octet is made up of eight bits or 1 byte.
Therefore every IP address is 32 binary bits (4 x 8 = 32) or 4 bytes.
Designed so that there would be enough IP addresses for the foreseeable future.
No one predicted the huge growth in IT
An example of how an IPv4 address appears in binary:
Each grouping of eight numbers is an octet and the four octets gives us a 32 bit IP address.
11000011. | 11110000. | 11001011. | 11111100
1st octet | 2nd octet | 3rd octet | 4th octet

## Slide 6: IPv4 Cont…
The reason for having a 32-bit address is because it was determined that this amount would be more than enough for many years to come.
Unfortunately, the huge growth of home and business computing was never anticipated.
IPv6 has several trillion available addresses that should last a few years into the future.
IP (version 4) addresses are broken into classes.
Depending upon how large your organization was, dictated which class of IP address you were given.
IP addresses are assigned by a group called the IANA (Internet Assigned Number Authority). You can also buy one from an ISP who has in turn bought a block form the IANA

## Slide 7: IP addressing: introduction
IP address: 32-bit identifier for host, router interface
interface: connection between host/router and physical link
  router’s typically have multiple interfaces
  host typically has one or two interfaces (e.g., wired Ethernet, wireless 802.11)
IP addresses associated with each interface
223.1.1.1
223.1.1.2
223.1.1.3
223.1.1.4
223.1.2.9
223.1.2.2
223.1.2.1
223.1.3.2
223.1.3.1
223.1.3.27
223.1.1.1 = 11011111 00000001 00000001 00000001
223
1
1
1

## Slide 8: IP addressing: introduction
Q: how are interfaces actually connected?
A: we’ll learn about that in chapter 5.
223.1.1.1
223.1.1.2
223.1.1.3
223.1.1.4
223.1.2.9
223.1.2.2
223.1.2.1
223.1.3.2
223.1.3.1
223.1.3.27
A: wired Ethernet interfaces connected by Ethernet switches
A: wireless WiFi interfaces connected by WiFi base station
For now: don’t need to worry about how one interface is connected to another (with no intervening router)

## Slide 9: Subnets
IP address:
  subnet part - high order bits
  host part - low order bits
what’s a subnet ?
  device interfaces with same subnet part of IP address
  can physically reach each other without intervening router
network consisting of 3 subnets
223.1.1.1
223.1.1.3
223.1.1.4
223.1.2.9
223.1.3.2
223.1.3.1
subnet
223.1.1.2
223.1.3.27
223.1.2.2
223.1.2.1

## Slide 10
IP address: 192.168.1.7
Subnet mask 255.255.255.0
Network IP 192.168.1.0
We can write it as 192.168.1.0/24
Usable IP addresses 2^8-2=254
192.168.1.255 is the broadcast address
IP address: 172.180.1.7
Subnet mask 255.255.0.0
Network IP 172.180.0.0
We can write it as 172.180.0.0/16
Usable IP addresses 2^16-2=65534
172.180.255.255 is the broadcast address

## Slide 11: Subnets
recipe
to determine the subnets, detach each interface from its host or router, creating islands of isolated networks
each isolated network is called a subnet
subnet mask: /24
223.1.1.0/24
223.1.2.0/24
223.1.3.0/24
223.1.1.1
223.1.1.3
223.1.1.4
223.1.2.9
223.1.3.2
223.1.3.1
subnet
223.1.1.2
223.1.3.27
223.1.2.2
223.1.2.1

## Slide 12: Subnets
how many?
223.1.1.1
223.1.1.3
223.1.1.4
223.1.2.2
223.1.2.1
223.1.2.6
223.1.3.2
223.1.3.1
223.1.3.27
223.1.1.2
223.1.7.3
223.1.7.1
223.1.8.3
223.1.8.1
223.1.9.1
223.1.9.2

## Slide 13: Classful Addressing
In the olden days…
  Class A: 0* (0xxxxxxx.*.*.*)
    Very large /8 blocks (e.g., MIT has 18.0.0.0/8)
  Class B: 10*
    Large /16 blocks (e.g,. Princeton has 128.112.0.0/16)
  Class C: 110*
    Small /24 blocks (e.g., AT&T Labs has 192.20.225.0/24)
  Class D: 1110*
    Multicast groups
  Class E: 11110*
    Reserved for future use (sounds a bit scary…)
And then, address space became scarce…

## Slide 14: Class A Addresses
These were given to the very largest organizations
  tremendous number of IP addresses since they owned more computers than everyone else.
Only use the first octet to identify the network number.
The remaining three octets are left for identifying the hosts on the network.
So the network is 10 and 2.5.4 is a host on that network.
In binary it would look like:
  nnnnnnnn.hhhhhhhh.hhhhhhhh.hhhhhhhh
Network.Host.Host.Host
10.2.5.4

## Slide 15: Cont …
Class A addresses are numbered from 1 to 126 in the first octet.
Network equipment identifies a class A address because the very first bit on the first octet has to be a 0.
  It cannot have a 1 in this bit position.
So the first network number is 1.
You would pronounce the above IP address as ten dot two dot five dot four.
128 | 64 | 32 | 16 | 8 | 4 | 2 | 1
0 | 0 | 0 | 0 | 0 | 0 | 0 | 1

## Slide 16: Cont …
The last possible network number is 127.
Use the powers of two rule:
  The first octet can have a possible 256 (2^8 = 256) networks.
  However, not allowed to use the first bit of the first octet, it is reserved for showing the 0 (binary) value.
  So this leaves us with 7 digits. 2^7–(1)gives us 127 networks.
  The full three octets to use for hosts so 8+8+8 bits gives us 2^24-(2) = 16,777,214 hosts per class A network.
128 | 64 | 32 | 16 | 8 | 4 | 2 | 1
0 | 1 | 1 | 1 | 1 | 1 | 1 | 1

## Slide 17: Cont …
Network number 127 cannot actually be used because the value 127.0.0.1 is reserved for troubleshooting.
  127.0.0.1 is known as a loopback address
  You can ping the loopback address to check if TCP/IP is working on your host.
We are not permitted to use 0 as a network number or the 127 which leaves us 126 available networks for class A addresses.
For the hosts we can start at number one until every single possible value is used up.

## Slide 18: Cont …
Example:
  10.0.0.1 is the first host, or in binary
  10.0.0.2 is the second host, or in binary:
00001010. | 00000000. | 00000000. | 00000001
10. | 0. | 0. | 1
00001010. | 00000000. | 00000000. | 00000010
10. | 0. | 0. | 2

## Slide 19: Cont …
  10.255.255.254 is the last host, or in binary:
Decimal notations are used so that it can be easy to write out the IP addresses and easy to remember.
Why can’t we have 10.255.255.255 as a host?
  Because when all the binary values have a 1 on the host part of the address this tells the network that it is a broadcast packet.
00001010. | 11111111. | 11111111. | 11111110
10. | 255. | 255. | 254

## Slide 20: Class B Addresses
They were reserved for large organizations that needed a lot of host numbers but not as many as the largest ones.
When a class B address was assigned to an organization it resulted in thousands of wasted host numbers.
They have to have the first two binary values on the first octet reserved with a 1 and a 0 next to it.
So the first network number is 128
  all the available network bits on the first octet turned off.
128 | 64 | 32 | 16 | 8 | 4 | 2 | 1
1 | 0 | 0 | 0 | 0 | 0 | 0 | 0

## Slide 21: Cont …
The last available class B network number is 191
  network bits have been turned on (on the first octet).
The first two octets for the network address the other two identify the hosts on the network.
For example, the address 130.24.5.2
  130.24 is the network number
  5.2 is a host on that network
The range of class B IP addresses is between 128 and 191.
128 | 64 | 32 | 16 | 8 | 4 | 2 | 1
1 | 0 | 1 | 1 | 1 | 1 | 1 | 1

## Slide 22: Cont …
Use the powers of two rule:
  The first two octets can have a possible 65536 (2^16 = 65536) networks.
  however, not allowed to use the first two bits of the first octet, they are reserved for showing the 10 (binary) value.
  So this leaves us with 6+8 digits. 2^14 gives us 16384 networks.
  The full two octets to use for hosts so 8+8 bits gives us 2^16 –(2) = 65534 hosts per class B network.

## Slide 23: Class C Addresses
Reserved for any other organization that was not large enough to warrant having a class A or B address.
It has the first three bits reserved so the network device can recognize it as such.
  The first three bits must show as 110.
The first network number is 192. All the other network bits are off (0).
128 | 64 | 32 | 16 | 8 | 4 | 2 | 1
1 | 1 | 0 | 0 | 0 | 0 | 0 | 0

## Slide 24: Cont …
And the last is 223. This time all the network bits are on (on the first octet).
An example of a class C address is 200.2.1.4
  200.2.1 is the network address
  .4 is a host on that network
There are lots of available network numbers to assign to companies
Limited amount of numbers free to use for the hosts on our networks.
128 | 64 | 32 | 16 | 8 | 4 | 2 | 1
1 | 1 | 0 | 1 | 1 | 1 | 1 | 1

## Slide 25: Cont …
For networks we have to take the first three bits (011) from the first octet giving us 5+8+8= 21 (network bits).
  2^21 = 2097152
For the hosts we have 2^8 giving us 256 (only 254 are usable though).

## Slide 26: Class D and E Addresses
Class D addresses are reserved for multicast traffic and cannot be used on your network.
  Multicast traffic is traffic sent to multiple hosts using one IP
    A live web cast of a rock concert would be an example of multicasting.
Class E addresses are reserved for experimental use only.
Addresses Reserved for Private Use
InterNIC has set aside certain addresses and have been reserved for private use only.
  For example, 127.0.0.1 is reserved for testing purposes only
Other include a list of addresses that are used only on private networks, not the Internet

## Slide 27: Cont …
If you would like to use TCP/IP on your internal network (intranet) and not use the Internet, the following addresses are suggested:
  Class A 10.0.0.0 through 10.255.255.255
  Class B 172.16.0.0 through 172.31.255.255
  Class C 192.168.0.0 through 192.168.255.255
Routers on the Internet will not route data from or to these addresses; they are for internal, private use only.
To use these addresses on an intranet and have access to the Internet, you must use a proxy server or Network Address Translation (NAT).

## Slide 28: Summary
Class A – first bit set to 0. Address range 1-126 (127 is reserved for testing) Network.Host.Host.Host
Class B – first bits set to 10. Address range 128-191 Network.Network.Host.Host
Class C – first bits set to 110. Address range 192-223 Network.Network.Network.Host
Class D – first bits set to 1110. Address range from 224-239
Class E – first bits set to 11110. Address range from 240-255
To recognize the address class of an IP, look at the first octet.
  10.1.2.1 = Class A, 190.2.3.4 = Class B, 220.3.4.2 = Class C

## Slide 29: IP Address Classes

## Slide 30: IP addressing: CIDR
CIDR: Classless InterDomain Routing
  subnet portion of address of arbitrary length
  address format: a.b.c.d/x, where x is # bits in subnet portion of address
11001000 00010111 00010000 00000000
subnet
part
host
part
200.23.16.0/23
Subnet mask 255.255.254.0

## Slide 31: Subnetting Example
An ISP has 134.16.0.0/16 and we need to have 4 subnets, find for each subnet:
The IP address range
Subnet mask
Broadcast address
Network address

## Slide 32
134.16.0.0/16
We need 4 subnets
The first subnet
134.16.00000000.00000000 134.16.0.0/18
Second subnet
134.16.01000000.00000000  134.16.64.0 /18
Third subnet
134.16.10000000.00000000 134.16.128.0/18
Fourth subnet
134.16.11000000.00000000 134.16.192.0/18

## Slide 33
The first subnet
134.16.00000000.00000000 134.16.0.0/18
First IP 134.16.00000000.00000001  134.16.0.1
Last IP address 134.16.00111111.11111110 134.16.63.254
Broadcast address  134.16.63.255

## Slide 34
Second subnet
134.16.0100000.00000000  134.16.64.0 /18
Network address 134.16.64.0
First IP address: 134.16.64.1
Last IP address 134.16.127.254
Broadcast IP address 134.16.127.255

## Slide 35
subnet | Network Address | Broadcast Address | First IP | Last IP
1 | 134.16.0.0 /18 | 134.16.63.255 | 134.16.0.1 | 134.16.63.254
2 | 134.16.64.0/18 | 134.16.127.255 | 134.16.64.0 | 134.16.127.254
3 | 134.16.128.0/18 | 134.16.191.255 | 134.16.128.1 | 134.16.191.254
4 | 134.16.192.0/18 | 134.16.255.255 | 134.16.192.1 | 134.16.255.254

## Slide 36: Subnetting Example
An ISP has 134.16.0.0/16 and we need to have 6 subnets, find for each subnet:
The IP address range
Subnet mask
Broadcast address
Network address

## Slide 37
First subnet
134.16.00000000.00000000
134.16.0.0/19
The new Subnet mask 255.255.224.0
First IP address 134.16.0.1
Last IP Address 134.16.31.254
Broadcast Address 134.16.31.255

## Slide 38
Second subnet
134.16.00100000.00000000
134.16.32.0/19
First IP address
134.16.32.1
Last IP address 134.16.63.254
Broadcast Address 134.16.63.255

## Slide 39: IP addresses: how to get one?
That’s actually two questions:
Q: How does a host get IP address within its network (host part of address)?
Q: How does a network get IP address for itself (network part of address)
How does host get IP address?
hard-coded by sysadmin in config file (e.g., /etc/rc.config in UNIX)
DHCP: Dynamic Host Configuration Protocol: dynamically get address from as server
  “plug-and-play”

## Slide 40: DHCP: Dynamic Host Configuration Protocol
goal: host dynamically obtains IP address from network server when it “joins” network
  can renew its lease on address in use
  allows reuse of addresses (only hold address while connected/on)
  support for mobile users who join/leave network
DHCP overview:
  host broadcasts DHCP discover msg [optional]
  DHCP server responds with DHCP offer msg [optional]
  host requests IP address: DHCP request msg
  DHCP server sends address: DHCP ack msg

## Slide 41: DHCP client-server scenario
223.1.1.1
223.1.1.2
223.1.1.3
223.1.1.4
223.1.2.9
223.1.2.2
223.1.2.1
223.1.3.2
223.1.3.1
223.1.3.27
DHCP server
223.1.2.5
arriving DHCP client needs
address in this network
Typically, DHCP server will be co-located in router, serving all subnets to which router is attached

## Slide 42: DHCP client-server scenario
DHCP server: 223.1.2.5
Arriving client
DHCP discover
src : 0.0.0.0, 68
dest.: 255.255.255.255,67
yiaddr: 0.0.0.0
transaction ID: 654
DHCP offer
src: 223.1.2.5, 67
dest: 255.255.255.255, 68
yiaddr: 223.1.2.4
transaction ID: 654
lifetime: 3600 secs
DHCP request
src: 0.0.0.0, 68
dest:: 255.255.255.255, 67
yiaddr: 223.1.2.4
transaction ID: 655
lifetime: 3600 secs
DHCP ACK
src: 223.1.2.5, 67
dest: 255.255.255.255, 68
yiaddr: 223.1.2.4
transaction ID: 655
lifetime: 3600 secs
Broadcast: is there a DHCP server out there?
Broadcast: I’m a DHCP server! Here’s an IP address you can use
Broadcast: OK. I would like to use this IP address!
Broadcast: OK. You’ve got that IP address!
The two steps above can be skipped “if a client remembers and wishes to reuse a previously allocated network address” [RFC 2131]

## Slide 43: DHCP: more than IP addresses
DHCP can return more than just allocated IP address on subnet:
  address of first-hop router for client
  name and IP address of DNS sever
  network mask (indicating network versus host portion of address)

## Slide 44: DHCP: example
Connecting laptop will use DHCP to get IP address, address of first-hop router, address of DNS server.
router with DHCP
server built into
router
DHCP REQUEST message encapsulated in UDP, encapsulated in IP, encapsulated in Ethernet
Ethernet frame broadcast (dest: FFFFFFFFFFFF) on LAN, received at router running DHCP server
Ethernet demux’ed to IP demux’ed, UDP demux’ed to DHCP
168.1.1.1
DHCP
UDP
IP
Eth
Phy
DHCP
DHCP
DHCP
DHCP
DHCP
DHCP
UDP
IP
Eth
Phy
DHCP
DHCP
DHCP
DHCP
DHCP

## Slide 45: DHCP: example
DCP server formulates DHCP ACK containing client’s IP address, IP address of first-hop router for client, name & IP address of DNS server
encapsulated DHCP server reply forwarded to client, demuxing up to DHCP at client
router with DHCP
server built into
router
DHCP
DHCP
DHCP
DHCP
DHCP
UDP
IP
Eth
Phy
DHCP
DHCP
UDP
IP
Eth
Phy
DHCP
DHCP
DHCP
DHCP
client now knows its IP address, name and IP address of DNS server, IP address of its first-hop router

## Slide 46: IP addresses: how to get one?
Q: how does network get subnet part of IP address?
A: gets allocated portion of its provider ISP’s address space
ISP's block 11001000 00010111 00010000 00000000 200.23.16.0/20
Subnet mask 255.255.240.0
ISP can then allocate out its address space in 8 blocks:
Organization 0 11001000 00010111 00010000 00000000 200.23.16.0/23
First ip 200.23.16.1 last ip address 200.23.17.254
Organization 1 11001000 00010111 00010010 00000000 200.23.18.0/23
Organization 2 11001000 00010111 00010100 00000000 200.23.20.0/23
... ….. …. ….
Organization 7 11001000 00010111 00011110 00000000 200.23.30.0/23
Subnet mask 255.255.254.0

## Slide 47: Hierarchical addressing: route aggregation
“Send me anything
with addresses
beginning
200.23.16.0/20”
200.23.16.0/23
200.23.18.0/23
200.23.30.0/23
Fly-By-Night-ISP
Organization 0
Organization 7
Internet
Organization 1
ISPs-R-Us
“Send me anything
with addresses
beginning
199.31.0.0/16”
200.23.20.0/23
Organization 2
.
.
.
.
.
.
hierarchical addressing allows efficient advertisement of routing information:

## Slide 48: Hierarchical addressing: more specific routes
“Send me anything
with addresses
beginning
200.23.16.0/20”
200.23.16.0/23
200.23.30.0/23
Fly-By-Night-ISP
Organization 0
Organization 7
Internet
200.23.18.0/23
Organization 1
ISPs-R-Us
“Send me anything
with addresses
beginning
199.31.0.0/16”
200.23.20.0/23
Organization 2
.
.
.
.
.
.
Organization 1 moves from Fly-By-Night-ISP to ISPs-R-Us
ISPs-R-Us now advertises a more specific route to Organization 1
200.23.18.0/23
Organization 1
“or 200.23.18.0/23”

## Slide 49: Hierarchical addressing: more specific routes
“Send me anything
with addresses
beginning
200.23.16.0/20”
200.23.16.0/23
200.23.30.0/23
Fly-By-Night-ISP
Organization 0
Organization 7
Internet
ISPs-R-Us
“Send me anything
with addresses
beginning
199.31.0.0/16”
200.23.20.0/23
Organization 2
.
.
.
.
.
.
Organization 1 moves from Fly-By-Night-ISP to ISPs-R-Us
ISPs-R-Us now advertises a more specific route to Organization 1
200.23.18.0/23
Organization 1
“or 200.23.18.0/23”

## Slide 50: IP addressing: last words ...
Q: how does an ISP get block of addresses?
A: ICANN: Internet Corporation for Assigned Names and Numbers http://www.icann.org/
  allocates IP addresses, through 5 regional registries (RRs) (who may then allocate to local registries)
  manages DNS root zone, including delegation of individual TLD (.com, .edu , …) management
Q: are there enough 32-bit IP addresses?
ICANN allocated last chunk of IPv4 addresses to RRs in 2011
NAT (next) helps IPv4 address space exhaustion
IPv6 has 128-bit address space
"Who the hell knew how much address space we needed?" Vint Cerf (reflecting on decision to make IPv4 address 32 bits long)

## Slide 51: Network layer: “data plane” roadmap
Network layer: overview
  data plane
  control plane
What’s inside a router
  input ports, switching, output ports
  buffer management, scheduling
IP: the Internet Protocol
  datagram format
  addressing
  network address translation
  IPv6
Generalized Forwarding, SDN
  match+action
  OpenFlow: match+action in action
Middleboxes

## Slide 52: NAT: network address translation
10.0.0.1
10.0.0.2
10.0.0.3
10.0.0.4
local network (e.g., home network) 10.0.0/24
138.76.29.7
rest of
Internet
datagrams with source or destination in this network have 10.0.0/24 address for source, destination (as usual)
all datagrams leaving local network have same source NAT IP address: 138.76.29.7, but different source port numbers
NAT: all devices in local network share just one IPv4 address as far as outside world is concerned

## Slide 53: NAT: network address translation
  all devices in local network have 32-bit addresses in a “private” IP address space (10/8, 172.16/12, 192.168/16 prefixes) that can only be used in local network
  advantages:
    just one IP address needed from provider ISP for all devices
    can change addresses of host in local network without notifying outside world
    can change ISP without changing addresses of devices in local network
    security: devices inside local net not directly addressable, visible by outside world

## Slide 54: NAT: network address translation
implementation: NAT router must (transparently):
  outgoing datagrams: replace (source IP address, port #) of every outgoing datagram to (NAT IP address, new port #)
      remote clients/servers will respond using (NAT IP address, new port #) as destination address
  remember (in NAT translation table) every (source IP address, port #) to (NAT IP address, new port #) translation pair
  incoming datagrams: replace (NAT IP address, new port #) in destination fields of every incoming datagram with corresponding (source IP address, port #) stored in NAT table

## Slide 55: NAT: network address translation
S: 10.0.0.1, 3345
D: 128.119.40.186, 80
1
10.0.0.4
138.76.29.7
1: host 10.0.0.1 sends datagram to 128.119.40.186, 80
NAT translation table
WAN side addr LAN side addr
138.76.29.7, 5001 10.0.0.1, 3345
…… ……
S: 128.119.40.186, 80
D: 10.0.0.1, 3345
4
S: 138.76.29.7, 5001
D: 128.119.40.186, 80
2
2: NAT router changes datagram source address from 10.0.0.1, 3345 to 138.76.29.7, 5001,
updates table
S: 128.119.40.186, 80
D: 138.76.29.7, 5001
3
3: reply arrives, destination address: 138.76.29.7, 5001
10.0.0.1
10.0.0.2
10.0.0.3

## Slide 56: NAT: network address translation
S: 192.168.1.16, 3345
D: 128.119.40.186, 80
1
192.168.1.1
138.76.29.7
1: host 10.0.0.1 sends datagram to 128.119.40.186, 80
NAT translation table
WAN side addr LAN side addr
138.76.29.7, 5001 192.168.1.16, 3345
138.76.29.7, 5002 192.168.1.16, 3346
…… ……
S: 128.119.40.186, 80
D: 192.168.1.16, 3345
4
S: 138.76.29.7, 5001
D: 128.119.40.186, 80
2
2: NAT router changes datagram source address from 10.0.0.1, 3345 to 138.76.29.7, 5001,
updates table
S: 128.119.40.186, 80
D: 138.76.29.7, 5001
3
3: reply arrives, destination address: 138.76.29.7, 5001
192.168.1.16
192.168.1.17
192.168.1.18

## Slide 57: NAT: network address translation
NAT has been controversial:
  routers “should” only process up to layer 3
  address “shortage” should be solved by IPv6
  violates end-to-end argument (port # manipulation by network-layer device)
  NAT traversal: what if client wants to connect to server behind NAT?
but NAT is here to stay:
  extensively used in home and institutional nets, 4G/5G cellular nets

## Slide 58: Network layer: “data plane” roadmap
Network layer: overview
  data plane
  control plane
Generalized Forwarding, SDN
  Match+action
  OpenFlow: match+action in action
Middleboxes
What’s inside a router
  input ports, switching, output ports
  buffer management, scheduling
IP: the Internet Protocol
  datagram format
  addressing
  network address translation
  IPv6

## Slide 59: Generalized forwarding: match plus action
1
2
0111
3
values in arriving
packet header
Review: each router contains a forwarding table
“match plus action” abstraction: match bits in arriving packet, take action
  generalized forwarding:
    many header fields can determine action
    many action possible: drop/copy/modify/log packet
forwarding table
(aka: flow table)
(aka: flow table)
  destination-based forwarding: forward based on dest. IP address

## Slide 60: Flow table abstraction
flow: defined by header field values (in link-, network-, transport-layer fields)
generalized forwarding: simple packet-handling rules
  match: pattern values in packet header fields
  actions: for matched packet: drop, forward, modify, matched packet or send matched packet to controller
  priority: disambiguate overlapping patterns
  counters: #bytes and #packets
Router’s flow table define router’s match+action rules
Flow table
match
action

## Slide 61: Flow table abstraction
flow: defined by header fields
generalized forwarding: simple packet-handling rules
  match: pattern values in packet header fields
  actions: for matched packet: drop, forward, modify, matched packet or send matched packet to controller
  priority: disambiguate overlapping patterns
  counters: #bytes and #packets
Flow table
match
action
1
2
3
4
* : wildcard
src=10.1.2.3, dest=*.*.*.* send to controller
src=1.2.*.*, dest=*.*.*.* drop
src = *.*.*.*, dest=3.4.*.* forward(2)

## Slide 62: OpenFlow: flow table entries
Match
Action
Stats
Forward packet to port(s)
Drop packet
Modify fields in header(s)
Encapsulate and forward to controller
Packet + byte counters
Header fields to match:
Ingress Port
Src MAC
Dst MAC
Eth Type
VLAN
ID
IP
ToS
IP Proto
IP Src
IP Dst
TCP/UDP Src Port
VLAN
Pri
TCP/UDP Dst Port
Link layer
Network layer
Transport layer

## Slide 63: OpenFlow: examples
IP datagrams destined to IP address 51.6.0.8 should be forwarded to router output port 6
Block (do not forward) all datagrams destined to TCP port 22 (ssh port #)
Block (do not forward) all datagrams sent by host 128.119.1.1
Destination-based forwarding:
*
*
*
*
*
*
51.6.0.8
*
*
*
port6
Switch
Port
MAC
src
MAC
dst
Eth
type
VLAN
ID
IP
Src
IP
Dst
IP
Prot
TCP
s-port
TCP
d-port
Action
VLAN
Pri
IP
ToS
*
*
*
*
*
*
*
*
*
*
*
*
Firewall:
drop
Switch
Port
MAC
src
MAC
dst
Eth
type
VLAN
ID
IP
Src
IP
Dst
IP
Prot
TCP
s-port
TCP
d-port
Action
VLAN
Pri
IP
ToS
22
*
Switch
Port
MAC
src
MAC
dst
Eth
type
VLAN
ID
IP
Src
IP
Dst
IP
Prot
TCP
s-port
TCP
d-port
Action
VLAN
Pri
IP
ToS
*
*
*
*
*
*
*
*
*
*
drop
*
128.119.1.1

## Slide 64: OpenFlow: examples
Layer 2 destination-based forwarding:
layer 2 frames with destination MAC address 22:A7:23:11:E1:02 should be forwarded to output port 3
*
*
*
*
*
*
*
*
*
port3
22:A7:23:
11:E1:02
*
*
Switch
Port
MAC
src
MAC
dst
Eth
type
VLAN
ID
IP
Src
IP
Dst
IP
Prot
TCP
s-port
TCP
d-port
Action
VLAN
Pri
IP
ToS

## Slide 65: OpenFlow abstraction
match+action: abstraction unifies different kinds of devices
Router
  match: longest destination IP prefix
  action: forward out a link
Switch
  match: destination MAC address
  action: forward or flood
Firewall
  match: IP addresses and TCP/UDP port numbers
  action: permit or deny
NAT
  match: IP address and port
  action: rewrite address and port

## Slide 66: OpenFlow example
Host h1
10.1.0.1
Host h2
10.1.0.2
Host h4
10.2.0.4
Host h3
10.2.0.3
Host h5
10.3.0.5
s1
s2
s3
1
2
3
4
1
2
3
4
1
2
3
4
Host h6
10.3.0.6
controller
Orchestrated tables can create network-wide behavior, e.g.,:
datagrams from hosts h5 and h6 should be sent to h3 or h4, via s1 and from there to s2

## Slide 67: OpenFlow example
IP Src = 10.3.*.*
IP Dst = 10.2.*.*
forward(3)
match
action
ingress port = 2
IP Dst = 10.2.0.3
ingress port = 2
IP Dst = 10.2.0.4
forward(3)
match
action
forward(4)
ingress port = 1
IP Src = 10.3.*.*
IP Dst = 10.2.*.*
forward(4)
match
action
Host h1
10.1.0.1
Host h2
10.1.0.2
Host h4
10.2.0.4
Host h3
10.2.0.3
Host h5
10.3.0.5
s1
s2
s3
1
2
3
4
1
2
3
4
1
2
3
4
Host h6
10.3.0.6
controller
Orchestrated tables can create network-wide behavior, e.g.,:
datagrams from hosts h5 and h6 should be sent to h3 or h4, via s1 and from there to s2

## Slide 68: Generalized forwarding: summary
“match plus action” abstraction: match bits in arriving packet header(s) in any layers, take action
  matching over many fields (link-, network-, transport-layer)
  local actions: drop, forward, modify, or send matched packet to controller
  “program” network-wide behaviors
simple form of “network programmability”
  programmable, per-packet “processing”
  historical roots: active networking
  today: more generalized programming:
  P4 (see p4.org).

## Slide 69: Network layer: “data plane” roadmap
Network layer: overview
What’s inside a router
IP: the Internet Protocol
Generalized Forwarding
Middleboxes
  middlebox functions
  evolution, architectural principles of the Internet

## Slide 70: Middleboxes
“any intermediary box performing functions apart from normal, standard functions of an IP router on the data path between a source host and destination host”
Middlebox (RFC 3234)

## Slide 71: Middleboxes everywhere!
enterprise
network
national or global ISP
datacenter
network
NAT: home, cellular, institutional
Firewalls, IDS: corporate, institutional, service providers, ISPs
Load balancers: corporate, service provider, data center, mobile nets
Caches: service provider, mobile, CDNs
Application-specific: service providers, institutional, CDN

## Slide 72: Middleboxes
initially: proprietary (closed) hardware solutions
move towards “whitebox” hardware implementing open API
  move away from proprietary hardware solutions
  programmable local actions via match+action
  move towards innovation/differentiation in software
SDN: (logically) centralized control and configuration management often in private/public cloud
network functions virtualization (NFV): programmable services over white box networking, computation, storage

## Slide 73: The IP hourglass
IP
TCP
UDP
HTTP
SMTP
QUIC
DASH
RTP
…
Ethernet
WiFi
Bluetooth
PPP
PDCP
…
copper radio fiber
Internet’s “thin waist”:
one network layer protocol: IP
must be implemented by every (billions) of Internet-connected devices
many protocols in physical, link, transport, and application layers

## Slide 74: The IP hourglass, at middle age
IP
TCP
UDP
HTTP
SMTP
QUIC
DASH
RTP
…
Ethernet
WiFi
Bluetooth
PPP
PDCP
…
copper radio fiber
Internet’s middle age “love handles”?
middleboxes, operating inside the network
NAT
NFV
Firewalls
caching

## Slide 75: Architectural Principles of the Internet
“Many members of the Internet community would argue that there is no architecture, but only a tradition, which was not written down for the first 25 years (or at least not by the IAB). However, in very general terms, the community believes that
RFC 1958
the goal is connectivity, the tool is the Internet Protocol, and the intelligence is end to end rather than hidden in the network.”
Three cornerstone beliefs:
simple connectivity
IP protocol: that narrow waist
intelligence, complexity at network edge

## Slide 76: Additional Chapter 4 slides

## Slide 77: DHCP: Wireshark output (home LAN)
Message type: Boot Reply (2)
Hardware type: Ethernet
Hardware address length: 6
Hops: 0
Transaction ID: 0x6b3a11b7
Seconds elapsed: 0
Bootp flags: 0x0000 (Unicast)
Client IP address: 192.168.1.101 (192.168.1.101)
Your (client) IP address: 0.0.0.0 (0.0.0.0)
Next server IP address: 192.168.1.1 (192.168.1.1)
Relay agent IP address: 0.0.0.0 (0.0.0.0)
Client MAC address: Wistron_23:68:8a (00:16:d3:23:68:8a)
Server host name not given
Boot file name not given
Magic cookie: (OK)
Option: (t=53,l=1) DHCP Message Type = DHCP ACK
Option: (t=54,l=4) Server Identifier = 192.168.1.1
Option: (t=1,l=4) Subnet Mask = 255.255.255.0
Option: (t=3,l=4) Router = 192.168.1.1
Option: (6) Domain Name Server
Length: 12; Value: 445747E2445749F244574092;
IP Address: 68.87.71.226;
IP Address: 68.87.73.242;
IP Address: 68.87.64.146
Option: (t=15,l=20) Domain Name = "hsd1.ma.comcast.net."
Message type: Boot Request (1)
Hardware type: Ethernet
Hardware address length: 6
Hops: 0
Transaction ID: 0x6b3a11b7
Seconds elapsed: 0
Bootp flags: 0x0000 (Unicast)
Client IP address: 0.0.0.0 (0.0.0.0)
Your (client) IP address: 0.0.0.0 (0.0.0.0)
Next server IP address: 0.0.0.0 (0.0.0.0)
Relay agent IP address: 0.0.0.0 (0.0.0.0)
Client MAC address: Wistron_23:68:8a (00:16:d3:23:68:8a)
Server host name not given
Boot file name not given
Magic cookie: (OK)
Option: (t=53,l=1) DHCP Message Type = DHCP Request
Option: (61) Client identifier
Length: 7; Value: 010016D323688A;
Hardware type: Ethernet
Client MAC address: Wistron_23:68:8a (00:16:d3:23:68:8a)
Option: (t=50,l=4) Requested IP Address = 192.168.1.101
Option: (t=12,l=5) Host Name = "nomad"
Option: (55) Parameter Request List
Length: 11; Value: 010F03062C2E2F1F21F92B
1 = Subnet Mask; 15 = Domain Name
3 = Router; 6 = Domain Name Server
44 = NetBIOS over TCP/IP Name Server
……
reply
request