## Slide 1: Fluid Mechanics ME 335 Afif Hasan Mechanical engineering
PUMPS

## Slide 2: Outline
Pump types
Specifications
Performance curves
Operating point
Pump selection
Affinity laws
Connecting pumps

## Slide 3: Function
Function: Fluids are moved by pumps, fans, blowers, and compressors. These use work to increase the mechanical energy of a fluid, which in turn can increase the flow rate (velocity), pressure, or elevation of the fluid.
Liquids are typically moved by pumps. Gases are moved by fans (large volume, small pressure difference), blowers (large volume, moderate pressure difference), or compressors (large pressure differences). Specialized equipment is also used to produce vacuums in process systems.

## Slide 4: Pumps types

## Slide 5: Reciprocating pumps
Positive displacement pumps operate by trapping a fixed volume of liquid then releasing it to a higher pressure by means of a piston or rotary gear.
Reciprocating pumps use a piston, plunger, or diaphragm to raise the pressure of a liquid.
The pumping chambers are surrounded by one-way valves so that liquid can only move in from the low pressure side and out from the high pressure side.
They are classed as "single acting" if fluid is moved only on the down stroke, or "double acting" if fluid is moved by both sides of the piston.

## Slide 6: Reciprocating pump
Because of the mechanism, these pumps produce a pulsating flow; but since flow is independent of head, they can be used to produce large pressure changes.
Reciprocating pumps are best for low volume, high head applications (up to 50000 psi). They cannot be used when pulsating flow is a problem.

## Slide 7: Diaphragm pumps
Diaphragm pumps are a sub-class of reciprocating pump.
The pumping chamber is separated from the moving parts by a flexible diaphragm.
Their chief advantage is that the fluid being pumped never comes in contact with the mechanism and eliminates leakage; thus they are good for toxic or very expensive liquids.
They cannot produce large head differences.
advantage is that the fluid being pumped never comes in contact with the mechanism and eliminates leakage; thus they are good for toxic or very expensive liquids.

## Slide 8: Rotary pumps
Rotary pumps use a gear, lobe, screw, cam, or vane to compress liquid.
Liquid enters through a gap between the rotating element and pump wall at a low pressure where it is trapped.
Then, as the element rotates, it squeezes the liquid out through a one-way valve on the opposite side of the casing.
Typically, rotary pumps are used in high head, low flow applications. They are good for high viscosity and low vapor pressure fluids.
The fluid pumped must be "lubricating"; solids cannot be present.

## Slide 9: Rotary pumps
Positive displacement rotary pumps also have their weaknesses.
Because of the nature of the pump, the clearance between the rotating pump and the outer edge must be very close, requiring that the pumps rotate at a slow, steady speed.
If rotary pumps are operated at high speeds, the fluids will cause erosion.

## Slide 10
Schematic design of positive-
displacement pumps: (a) reciprocating
piston or plunger,
(b) External gear pump,
(c) double-screw pump,
(d) sliding vane,
(e) Three-lobe pump,
( f ) double circumferential
piston,
(g) flexible-tube squeegee.

## Slide 11: Vane pump Scroll pump

## Slide 12: Screw pump

## Slide 13: Kinetic energy pumps
Axial
Radial
Mixed

## Slide 14: Axial pump
Axial flow pumps differ from radial flow in that the fluid enters and exits along the same direction parallel to the rotating shaft.
Axial flow pumps operate at much lower pressures and higher flow rates than radial flow pumps.

## Slide 15: Mixed flow pumps
Mixed flow pumps, as the name suggests, function as a compromise between radial and axial flow pumps, the fluid experiences both radial acceleration and lift and exits the impeller somewhere between 0-90 degrees from the axial direction.
As a consequence mixed flow pumps operate at higher pressures than axial flow pumps while delivering higher discharges than radial flow pumps

## Slide 16: Centrifugal pump
A centrifugal pump increases liquid pressure by increasing its velocity by means of a rotating impeller.
Liquid enters at the center of the impeller, is accelerated by the impeller vanes, and leaves through the side of the pump casing. Changing direction by 90o

## Slide 17: Centrifugal pump

## Slide 18: Pumps Specifications
Pumps are commonly rated by horsepower, flow rate, outlet pressure in feet (or metres) of head, inlet suction in suction feet (or metres) of head.
The performance of a centrifugal pump can be shown graphically on a characteristic curve. A typical characteristic curve shows the total dynamic head, brake horsepower, efficiency, and net positive Suction head all plotted over the capacity range of the pump.

## Slide 19: Head
"Head" is just a way of expressing pressure -- specifically, in terms of the height of a column of liquid that would produce the same pressure.
The main reason for using head instead of pressure to measure a centrifugal pump's energy is that the pressure from a pump will change if the specific gravity (weight) of the liquid changes, but the head will not change. Since any given centrifugal pump can move a lot of different fluids, with different specific gravities, it is simpler to discuss the pump's head and forget about the pressure.

## Slide 20: Head
STATIC DISCHARGE HEAD is the vertical distance in feet between the pump centerline and the point of free discharge or the surface of the liquid in the discharge tank.
TOTAL STATIC HEAD is the vertical distance in feet between the free level of the source of supply and the point of free discharge or the free surface of the discharge liquid.

## Slide 21: Friction head
FRICTION HEAD (hf) is the head required to overcome the resistance to flow in the pipe and fittings. It is dependent upon the size, condition and type of pipe, number and type of pipe fittings, flow rate, and nature of the liquid.
  hf = (L/d)(V2 /g) f

## Slide 22: Capacity
Capacity means the flow rate with which liquid is moved or pushed by the pump to the desired point in the process.
It is commonly measured in either gallons per minute (gpm) or cubic meters per hour (m3/hr), or liter per minute ( l/min).

## Slide 23: H- Q curve

## Slide 24: Power
The power added to the fluid flow by the pump (Po), is defined using SI units by:
where:
Po is the output power of the pump (W)
ρ is the fluid density (kg/m3)
g is the gravitational constant (9.81 m/s2)
H is the energy Head added to the flow (m)
Q is the flow rate (m3/s)

## Slide 25: Power
Power is more commonly expressed as kW (103 W) or horsepower (multiply kW by 0.746),
hp is equivalent to the pressure head added by the pump when the suction and discharge pipes are of the same diameter.
The power required to drive the pump is determined by dividing the output power by the pump efficiency.

## Slide 26: Typical centrifugal pump curves

## Slide 27: Power, efficiency, head curves

## Slide 28: Pump driver
All pumps must have a driver to supply power.
Typically, drivers are electric motors , gas/Petrol/ Diesel engines may be used in remote locations.
As a general rule, motors are single speed devices -- variable speed motor drivers are expensive.

## Slide 29: Pump efficiency
Pump efficiency is defined as the ratio of the power imparted on the fluid by the pump in relation to the power supplied to drive the pump.
Its value is not fixed for a given pump, efficiency is a function of the discharge and therefore also operating head.
For centrifugal pumps, the efficiency tends to increase with flow rate up to a point midway through the operating range (peak efficiency) and then declines as flow rates rise further

## Slide 30: Power, efficiency, head curves

## Slide 31: Net Positive Suction Head
Net Positive Suction Head Available is a function of the system in which the pump operates.
It is the excess pressure of the liquid in feet absolute over its vapor pressure as it arrives at the pump suction,
to be sure that the pump selected does not cavitate. It is calculated based on system or process conditions.
NPSH as the total suction head in feet absolute, determined at the suction nozzle and corrected to datum, less the vapor pressure of the liquid in feet absolute.

## Slide 32: Net Positive Suction Head - NPSH
Net Positive Suction Head - NPSH
The Net Positive Suction Head - NPSH - can be expressed as the difference between the Suction Head, and the Liquids Vapor Head as
NPSH = hs - hv (3)
NPSH = [ps / γ + vs2 / 2 g] - pv / γ (3b)
Where NPSH = Net Positive Suction Head (m, in)
where pi and Vi are the pressure and velocity at the pump inlet and pv is the vapor pressure of the liquid.

## Slide 33
Net Positive Suction Head

## Slide 34: Net Positive Suction Head
Fig. 11.7 Measured-performance curves for two models of a centrifugal water pump: (a) basic casing with three impeller sizes

## Slide 35: Net Positive Suction Head
Measured-performance curves for two models of a centrifugal water pump: (b) 20 percent larger casing with three larger impellers at slower speed.

## Slide 36: EXAMPLE 11.2 p. 727 White
The 32-in pump of Fig. 11.7a is to pump 24,000 gal/min of water at 1170 r/min from a reservoir whose surface is at 14.7 lbf/in2 absolute. If head loss from reservoir to pump inlet is 6 ft, where should the pump inlet be placed to avoid cavitation for water at (a) 60°F, pv= 0.26 lbf/in2 absolute, SG =1.0 and (b) 200°F, pv =11.52 lbf/in2 absolute, SG= 0.9635?
If the pump inlet is placed at a height Zi above a reservoir whose free surface is at pressure pa, we can use energy equation to rewrite NPSH as
(P1/Ɣ) +z1 +(V12 /2g) = (PB/Ɣ) +zB +(VB2 /2g) + hf
(Pa/Ɣ) = (Pi/Ɣ) +zi +(Vi2 /2g) + hfi

## Slide 37: EXAMPLE 11.2 p. 727 White
For either case read from Fig. 11.7a at 24,000 gal/min that the required NPSH is 40 ft. For this case gama = 62.4 lbf/ft3.
The pump must be placed at least 12.7 ft below the reservoir surface to avoid cavitation.

## Slide 38: EXAMPLE 11.2 p. 727 White
B) At 200F Pv=11.52psi for this case ɣ= 62.4(0.9635)= 60.1 lbf/ft3. Equation (11.20) applies again with the higher p.

## Slide 39: Operating point
The operating point is at the intersection of the system curve and pump curve.
The point where the pump operates on its curve is dependent upon the characteristics of the system in which it is operating, commonly called the System Head Curve
This representation is in a graphic form and, since friction losses vary as a square of the flow rate, the system curve is parabolic in shape;
(P1/Ɣ) +z1 +(V12 /2g) = (PB/Ɣ) +zB +(VB2 /2g) + hf + hminor + hp

## Slide 40: System curve
hp = ∆z + C1 V2/2g
hp = ∆ z + C2 Q2
Since
V= 4 Q/d2*π
(P1/Ɣ) +z1 +(V12 /2g) = (PB/Ɣ) +zB +(VB2 /2g) + hf + hminor + hp
If P1 =P2 = Atmospheric and V1 =V2

## Slide 41: System head curve
The flow rate can be reduced by throttling the discharge valve.
Hence hf will increase.

## Slide 42: Operating point

## Slide 43
Fig. 11.17 Illustration of pump operating points for three types of
system-head curves.

## Slide 44: Matching Pumps to System Characteristics
The ultimate test of a pump is its match with the operating-system characteristics.
Physically, the system head must match the head produced by the pump, and this intersection should occur in the region of best efficiency.

## Slide 45: EXAMPLE 11.6
We want to use the 32-in pump of Fig. 11.7a at 1170 r/min to pump water at 60°F from one reservoir to another 120 ft higher through 1500 ft of 16-in-ID pipe with friction factor f = 0.030.
(a) What will the operating point and efficiency be?
For reservoirs the initial and final velocities are zero; thus the system head is

## Slide 46: EXAMPLE 11.6
plot Eq. (2) on Fig. 11.7a and see where it intersects the 32-in pump-head curve, as in Fig. E11.6. A graphical solution gives approximately
H= 430 ft , Q= 15,000 gal/min
An analytic solution is possible if we fit the pump-head curve to a parabola;
at the operating point

## Slide 47: Example pump selection

## Slide 49: Selecting a pump
When selecting a pump, consider the following factors;
Nature of liquid (viscosity, toxicity, slurry containing solids etc)
Required capacity ( flow , discharge or Q)
Required total head , hp
Suction conditions
Discharge conditions
Types of power supply ( electricity AC/DC, mechanical , )
Cost of pump and operation.

## Slide 50: Selecting a pump
Pump is selected for specific application based on the pump head, hp; the flow rate, Q and taken into consideration NPSH

## Slide 53: Selecting type of pump

## Slide 54: Pumps in parallel
Two or more pumps are arranged in parallel, their resulting performance curve is obtained by adding their flowrates at the same head.

## Slide 55: Pumps in series
Two (or more) pumps are arranged in serial, their resulting pump performance curve is obtained by adding heads at the same flow rate.

## Slide 56
Slides ( # 59 to 67 ) on pumps scaling are not required

## Slide 57: Dimensionless Pump Performance
Head output variables H and brake horsepower should be dependent upon discharge Q, impeller diameter D, and shaft speed n, at least. Other possible parameters are the fluid density , viscosity , and surface roughness ;
For each function in there are seven variables and three primary dimensions (M, L, and T); hence we expect 7 - 3 = 4 dimensionless groups. You can verify as an exercise that appropriate dimensionless forms;
The quantities ρnD2/ and ϵ/D are recognized as the Reynolds number and roughness ratio, respectively.

## Slide 58: Dimensionless Pump Performance
Three new pump parameters have arisen

## Slide 59: Similarity Rules
in correlating pump data leads to simple rules for comparing pump performance.
If pump 1 and pump 2 are from the same geometric family and are operating at homologous points (the same dimensionless position on a chart such as Fig. 11.8), their flow rates, heads, and powers will be related as follows

## Slide 60: Affinity laws
The affinity laws express the mathematical relationship between the several variables involved in pump performance. They apply to all types of centrifugal and axial flow pumps.
With impeller diameter D held constant and N varied:
Where:
Q = Capacity, GPM H = Total Head, Feet BHP = Brake Horsepower N = Pump Speed, RPM

## Slide 61: Affinity laws
With speed N held constant, D is varied:

## Slide 62: Example
To illustrate the use of these laws, refer to Fig. 8 below. It shows the performance of a particular pump at 1750 RPM with various impeller diameters. This performance data has been determined by actual tests by the manufacturer. Now assume that you have a 13" maximum diameter impeller, but you want to belt drive the pump at 2000 RPM.

## Slide 63: Example
The affinity laws listed under 1 above will be used to determine the new performance, with N1 =1750 RPM and N2 = 2000 RPM.
The first step is to read the capacity, head, and horsepower at several points on the 13" dia. curve in Fig. 9 below. For example, one point may be near the best efficiency point where the capacity is 300 GPM, the head is 160 ft, and the BHP is approx. 20 hp.

## Slide 64: Example

## Slide 65: Example