## Slide 1: Thermal Fluid Engineering ENMC4411 Chapter 10 COOLING OF ELECTRONIC EQUIPMENT
Afif Akel Hasan
Mechanical & Mechatronics Engineering Department
Birzeit University

## Slide 2: Outline
Introduction
Cooling Load of Electronic Equipment
Electronics Cooling in Different Applications
Conduction Cooling
Air Cooling: Natural Convection
Air Cooling: Forced Convection

## Slide 3: Junctions
Narrow band where two different regions of a semiconductor (such as the p-type and n-type regions) come in contact is called a junction.
That is, junctions are the sites of heat generation and thus the hottest spots in a component.
In silicon-based semiconductor devices, the junction temperature is limited to 125°C for safe operation.
However, lower junction temperatures are desirable for extended life and lower maintenance costs.
Electronic components are inherently reliable, if components operated at room temperature. But electronic components are observed to fail under prolonged use at high temperatures.
A rule of thumb is that the failure rate of electronic components is halved for each 10°C reduction in their junction temperature

## Slide 4: Cooling load of electronic equipment
The first step in the selection and design of a cooling system is the determination of the heat dissipation, which constitutes the cooling load.
The heat dissipation or cooling load of an electronic device is equal to its power consumption. That is, Q=W = VI= I2 R

## Slide 5: Cooling techniques
For steady operation power rating of a device or component is given, the heat flux is determined by dividing the power rating by the exposed surface area of the device or component.
Then suitable heat transfer mechanisms can be determined from Figure below, from the requirement that the temperature difference between the surface of the device and the surrounding medium not exceed the allowable maximum value.
Heat fluxes that can be attained at specified temperature differences with various heat transfer mechanisms and Fluids.

## Slide 6: Conduction in Chip Carriers
The chip is attached to the lead frame with a highly conductive bonding material that provides a low-resistance path for heat flow from the chip to the lead frame.
There is no metal connection between the lead frame and the leads, since this would short-circuit the entire chip. Therefore, heat flow from the lead frame to the leads is through the dielectric case material such as plastic or ceramic.
Heat is then transported outside the electronic device through the leads.

## Slide 7: Total resistant of a chip
Q equals power consumption of chip, then

## Slide 9
EXAMPLE 15–4 Predicting the Junction Temperature of a Device
A fan blows air at 30°C and a velocity of 200 m/min over a 1.2-W plastic DIP with 16 leads mounted on a PCB, as shown in Figure 15–24. Using data from Figure 15–23, determine the junction temperature of the electronic device.
What would the junction temperature be if the fan were to fail?
SOLUTION A plastic DIP with 16 leads is cooled by forced air. Using data supplied by the manufacturer, the junction temperature is to be determined.
Analysis The junction-to-ambient thermal resistance of the device with 16 leads corresponding to an air velocity of 200 m/min is determined from Figure 15–23 to be
Rjunction-ambient = 55°C/W
Then the junction temperature can be determined from Eq. 15-9 to be
Tjunction = Tambient +QRjunction-ambient = 30°C + (1.2 W)(55°C/ W) = 96°C
When the fan fails, the airflow velocity becomes zero. The total thermal resistance in this case Rjunction-ambient = 70°C/W
which gives
Tjunction = Tambient +QRjunction-ambient = 30°C + (1.2 W)(70°C/ W) =114°C

## Slide 10: Heat frame
In applications where direct cooling of circuit boards by passing air or a dielectric liquid over the electronic components is not allowed, and the junction temperatures are to be maintained relatively low to meet strict safety requirements, a thick heat frame is used instead of a thin layer of copper cladding.
When a heat frame is used, heat conduction in the epoxy layer of the PCB is through its thickness instead of along its length.

## Slide 11: Air cooling: natural convection and radiation
Low-power electronic systems are conveniently cooled by natural convection and radiation.
Natural convection cooling is very desirable, since it does not involve any fans that may break down.
Electronic components or PCBs placed in enclosures such as a TV cooled by natural convection by providing a sufficient number of vents on the case to enable the cool air to enter and the heated air to leave the case freely.
Radiation heat transfer between a surface at temperature Ts completely surrounded by a much larger surface at temperature Tsurr can be expressed as

## Slide 12: Forced internal convection
The amount of heat absorbed by the air becomes equal to the amount of heat rejected (or power dissipated) by the electronic components in the enclosure, and can be expressed as
Q =m · Cp(Tout - Tin)
where Q is the rate of heat transfer to the air; Cp is the specific heat of air; Tin and Tout are the average temperatures of air at the inlet and exit of the enclosure, respectively; and m · is the mass flow rate of air.
It is considered a good design practice to limit the temperature rise of air to 10°C and the maximum exit temperature of air to 70°C. In a properly designed forced-air-cooled system, this results in a maximum component surface temperature of under 100°C.

## Slide 13: Fan Selection
A fan at a fixed speed (or fixed rpm) will deliver a fixed volume of air regardless of the altitude and pressure.
Variable-speed fans that automatically increase speed when the air density decreases are available to avoid such problems.
Electronic systems are usually equipped with thermal cutoff switches to prevent overheating due to inadequate airflow rate or the failure of the cooling fan.
Fan can be place at inlet or exit of the box.

## Slide 14: Fan at inlet
The generally preferred location is the inlet. A fan placed at the inlet draws air in and pressurizes the electronic box and prevents air infiltration into the box from cracks or other openings.
install a filter at the inlet to clean the air from all the dust and dirt before they enter the box. This allows the electronic system to operate in a clean environment. Also, a fan placed at the inlet handles cooler and thus denser air, which results in a higher mass flow rate for the same volume flow rate or rpm.
Disadvantage associated with having a fan mounted at the inlet is that the heat generated by the fan and its motor is picked up by air on its way into the box, which adds to the heat load of the system.

## Slide 15: Fan at exit
the heat generated by the fan and its motor is immediately discarded to the atmosphere without getting blown first into the electronic box.
However, a fan at the exit creates a vacuum inside the box, which draws air into the box through inlet vents as well as any cracks and openings.
the air is difficult to filter, and the dirt and dust that collect on the components undermine the reliability of the system
A fan placed at the exit of an electronic box draws in air as well as contaminants in the air through cracks

## Slide 16: Fan sizing
Two primary considerations in the selection of the fan: the static pressure head of the system, which is the total resistance an electronic system offers to air as it passes through, and the volume flow rate of the air.
The required airflow rate for a system can be determined from heat transfer requirements alone, using the design heat load of the system and the allowable temperature rise of air.
Q =m · Cp(Tout - Tin)
Then the flow resistance of the system at this flow rate can be determined analytically or experimentally.
Knowing the flow rate and the needed pressure head, it is easy to select a fan from manufacturers’ catalogs that will meet both of these requirements.

## Slide 20: Guidelines for forced-air cooling of electronic systems
1. Before deciding on forced-air cooling, check to see if natural convection cooling is adequate. If it is, which may be the case for low-power systems, incorporate it and avoid all the problems associated with fans.
2. Select a fan that is neither too small nor too large. An undersized fan may cause the electronic system to overheat and fail. An oversized fan will definitely provide adequate cooling, but it will needlessly be larger and more expensive and will consume more power.
3. If the temperature rise of air due to the power consumed by the motor of the fan is acceptable, mount the fan at the inlet of the box to pressurize the box and filter the air to keep dirt and dust out.
4. Position and size the air exit vents so that there is adequate airflow throughout the entire box. The total exit areas should be at least as large as the inlet flow area to avoid the choking of the airflow, which may result in a reduced airflow rate.

## Slide 21
5. Place the most critical electronic components near the entrance, where the air is coolest. Place the non-critical components that consume a lot of power near the exit.
6. Arrange the circuit boards and the electronic components in the box such that the resistance of the box to airflow is minimized and thus the flow rate of air through the box is maximized for the same fan speed. Make sure that no hot air pockets are formed during operation.
7. Try to avoid any flow sections that increase the flow resistance of the systems, such as unnecessary corners, sharp turns, sudden expansions and contractions, and very high velocities (greater than 7 m/s), since the flow resistance is nearly proportional to the flow rate. Also, avoid very low velocities since these result in a poor heat transfer performance and allow the dirt and the dust in the air to settle on the components.
Guidelines for forced-air cooling of electronic systems

## Slide 22
8. Arrange the system such that natural convection helps forced convection instead of hurting it. For example, mount the PCBs vertically, and blow the air from the bottom toward the top instead of the other way around.
9. When the design calls for the use of two or more fans, a decision needs to be made about mounting the fans in parallel or in series. Fans mounted in series will boost the pressure head available and are best suited for systems with a high flow resistance. Fans connected in parallel will increase the flow rate of air and are best suited for systems with small flow resistance.
Guidelines for forced-air cooling of electronic systems