## Slide 1: Thermal Fluid Engineering ENMC4411 Chapter 2 Fluid Statics
Afif Akel Hasan
Mechanical & Mechatronics Engineering Department
Birzeit University

## Slide 2: Outline
Fluids
Units & dimensions
Properties of fluids
Pressure variations
Pressure forces
Buoyancy

## Slide 3: Fluid
Matter consist of two states ; fluid and solid . A solid can resist sheer stress by a static deformation . The fluid move and deforms continuously as long as sheer stress is applied.
A fluid continues to flow for as long as the force is applied and will not recover its original form when the force is removed.
Shear force : force component tangent to the surface .
Shear stress is the sheer force per unit area τ = F/area .

## Slide 4: Fluid Mechanics
Fluid Mechanics : is the study of the fluids either in motion or at rest and the effects of the fluid upon the boundaries. Gases and liquid are classified as fluids .
Fluid at rest : fluid statics
Fluid in motion : fluid dynamics

## Slide 5: Fluids
fluid of two classes: liquids and gases .
A liquid composed of relatively closed – packed molecules with strong cohesive forces ,while gases are widely spaced molecules with negligible cohesive forces .
A gas has no definite volume

## Slide 6: Engineering Application
Examples include breathing , blood flow, heart, swimming,
Machinery: Pumps, fans, turbines
Ships, cars , air planes , plane engines , jets …

## Slide 7: Dimensions and Units
Primary dimensions: from which all other dimensions can be derived : mass, length, time and temperature , for ones used in fluid mechanics see Table (1.1) P. 8 .

## Slide 8: Secondary dimensions
Derived or constructed from combinations of these four primary dimensions eg .
Acceleration L/T2 = LT-2 dv/dt
Force F = m a (Newton's 2nd law)
F = M L T-2
i.e 1N = 1kg .m/s2
See table 1.2 p .9 for some secondary dimensions.

## Slide 9: Primary unit systems
  There are three primary unit systems in use:
    the International System of Units (SI units - kg, N, m, s, K)
    the English Engineering System of Units (commonly called English units - lbm, lbf, ft, s, R)
    the British Gravitational System of Units (BG - slug, lbf, ft, s, oR)
  Units must always have numbers associated with them.
  For example, length is a dimension, but it is measured in units of feet (ft) or meters (m).

## Slide 10: Secondary dimensions

## Slide 11: Outline
Fluids
Units & dimensions
Properties of fluids
Pressure variations
Pressure forces
Buoyancy

## Slide 12: Thermodynamic Properties of a fluid
Most common properties
Pressure P
Density ρ
Temperature T
Others for work and energy calculations:
Internal energy u
Enthalpy h = u +P/r
Specific heat Cp , Cv
Entropy s
Viscosity μ
Thermal conductivity k
Two properties such as ( P,T) are sufficient to fix the value of all other properties for pure substances.

## Slide 13: Pressure & temperature
Pressure: pressure is the stress at a point in a static fluid, or force per unit normal area P = Fnormal / Aarea .
1 atmosphere = 101300 Pa = 101.30 kPa= 14.7 PSI
Temperature : a measure of the internal energy level of a fluid,
Centigrade ( Celsius) and absolute K = C +273.16 .

## Slide 14: Fluid density
Density : mass per unit volume , symbol ( ρ )
ρ = m/v [ kg/m3 ]
Density is nearly constant for liquids, while increasing proportional to pressure of gases .
Liquids are treated as incompressible fluid (density doesn’t change with changing pressure ) .
e.g water density 1000kg/m3, air density 1.2 kg/m3 at 300 K 1 atm.
Mercury 13600 kg/m3.

## Slide 15: Specific gravity
Specific gravity SG : a ratio of a fluid density to standard reference fluid.
Reference fluids: water ( for liquids ) and air for gases .
SG gas = ρ gas / ρ air = ρ gas / 1.205 kg/m3
SG liquid = ρ liquid / ρ water = ρ liquid / 998 kg/m3
e.g SG Hg = 13580 / 998 = 13.6

## Slide 16: Specific weight
Specific weight: denoted by “ ɣ “ is the weight per unit volume ɣ = ρ g
since ɣ = mg /V = ρ g .
Hence units of [ɣ ] are N / m3 or lbf/ ft3 .
e.g ɣ air = 1.205*9.8 = 11.8 N/m3 = 0.0752 lbf/ft3
  at 20 C ɣ water = 9.807 *998 = 9790 N/m3 = 62.4 lbf/ft3
To remember: ɣ air = 10 N/ m3 , ɣ water = 10kN/m3

## Slide 17: Potential and Kinetic Energy
Energy stored in a system by molecular, activity and molecular bonding forces is denoted as internal energy .
Potential energy equals the work required to move up the system mass ‘m’ from one elevation to another one against the gravity field . PE = mg ∆z
Kinetic energy equals the work required to change the speed of the ‘m’ from zero to velocity V , its value is ½mV2 .
The total storage energy per unit mass in fluid mechanics is given as e = u + ½V2 + gz

## Slide 18: State relation of gases
Pure substance for a single – phase pure substance e.g water in liquid phase . Air can be consider to be a pure substance, two properties fixes state and value of other properties V = f( T,P ).
Gases at high temperature and low pressure are treated as perfect and ideal gases intermolecular forces are negligible.
Ideal gas PV = mRT
P = (m/V ) RT = ρRT
PV = n T
= universal gas constant = 8314 m2/s2.K
R = /( M.wt)  for air Mwt = 28.97
e.g Rair = 287 m2/s2 .K
standard air density @ 25 C Patm = 101300Pa
ρair = P/(RT) = 10300 [N/m2 ]/ (287[m2/s2.K] * 298[k]) = 1.205 kg/m3

## Slide 19: Specific heat
for gases
Specific heat at constant volume Cv = ( du/dt )v
Specific heat at constant pressure Cp = ( dh/dt )p
Specific heat ratio K = (Cp /Cv ) > 1
For air k=1.4
For ideal gases internal energy and enthalpy are only function of temperature.
u = f(t) , h = f(t)
dh = Cpo dT  ∆h = ∫ Cpo dT
du = Cvo dT  ∆u = ∫ Cvo dT

## Slide 20: Vapor pressure
It is the pressure developed above the liquid when liquid in a closed container or pressure at which liquid boils .
Vapor pressure is a function of temperature e.g for water
at 100 o C Pvapor =1 atm = 101.30kPa .
at 50 o C Pvapor = 12.350 kPa
Vapor pressure of water.

## Slide 21: Cavitation
Cavitation occurs when pressure is lower than vapor pressure at given temperature of liquid ( liquid will flash into vapor ).
For cavitation , dimensionless parameter called cavitation number is used
Ca = (Psys - P­v )/ ½ρV2
Where : Psys = system pressure
Pv = vapor pressure
V = flow velocity
Critical cavitation number : value of Ca below which cavitation ( bubbles formation ) Take place in a flow.

## Slide 22: Surface Tension
A liquid will form an interface with a second liquid or a gas .
Surface tension results from cohesive forces, between similar molecules , and “adhesive” force between unlike molecules .
At interface cohesive force from below ( liquid ) exceeds adhesive force ( gas/liquid ) hence resulting in surface tension .
Surface tension results in formation of liquid droplets, bubbles, and capillary action .
It is measured by stretching force required to form the film , surface energy per unit length .
Unit of [s] : F/L SI N/m or lbf/ft
e.g water /air s = 0.073N/m
air / mercury s = 0.48 N/m

## Slide 23: Contact angle
Surface tension occurs during a gas-liquid interface, but if that interface comes in contact with a solid surface - such as the walls of a container - the interface usually curves up or down near that surface. Such a concave or convex surface shape is known as a meniscus.

## Slide 24: Capillary Action
contact angle ϴ appears when liquid intersect
with the a solid surface .
If ϴ < 90 wetting ( wets the solid )
If ϴ > 90 Non wetting liquid .
capillary action when liquid rises or falls in capillary tubes .
it is caused by surface tension and by the relative values of adhesive ( liquid to solid ) and cohesive force ( between the liquid molecules ).

## Slide 25: Example 1.9 p 31
Surface tension force at inter-face must balance the weight of the column of liquid of height (h )
(2σ π R) cosϴ = ɣ π R2 h
then h = (2 σ cosϴ /ɤR)
h > 0 positive if ϴ < 90
h < 0 negative if ϴ > 90
a ) e.g for water – air –glass ϴ = 0 σ = 0.073 N/m
ρ = 1000kg/m3 R = 1 mm
h = 2(0.073cos ϴ / (1000*9.81*0.001) = 0.015 m = 1.5 cm .
b ) for mercury – air – glass
ϴ = 130, σ = 0.48 N/m ρ = 13600 kg /m3
R = 1 mm
h = 2*0.48 *cos130 / 13600*9.81*0.001 = -0.46

## Slide 26: Basic Flow-Analysis Techniques
There are three basic ways to attack a fluid-flow problem;
  Control-volume, or integral analysis (Chap. 3)
  Infinitesimal system, or differential analysis (Chap. 4)
  Experimental study, or dimensional analysis (Chap. 5)
The flow must satisfy the three basic laws of mechanics plus a thermodynamic state relation and associated boundary conditions.
  Conservation of mass (continuity)
  Linear momentum (Newton’s second law)
  First law of thermodynamics (conservation of energy)
  A state relation like f(p, T)
  Appropriate boundary conditions at solid surfaces, interfaces, inlets, and exits

## Slide 27: Outline
Fluids
Units & dimensions
Properties of fluids
Pressure variations
Pressure forces
Buoyancy

## Slide 28: Pressure at a point
It can be shown that at any point in a fluid the pressure is the same in all directions .
Px = Py = Pz

## Slide 29: Pressure variation
Pressure in a continuously distributed uniform static fluid varies only with vertical distance and is independent of the shape of the container.
The pressure is the same at all points on a given horizontal plane in the fluid.
The pressure increases with depth in the fluid.

## Slide 30: Pressure scale
Absolute pressure at complete vacuum
Pgauge = P absolute - Patmosphere
Or
Pabs = Patm + Pgauge
Patm = 760 mm Hg
= 101.325kPa
= 14.7 psi
Bourdon gauge : measures gauge pressure
Barometer : measure atmospheric pressure

## Slide 31: Bourdon gauge

## Slide 32: Incompressible fluid
Hydrostatic pressure distribution
( dp/dz ) = -ɣ = -ρg
P2 –P1 = - ɣ (z2-z1 )
P2 = P1 + ɣ (z1-z2)
P2 = P1 + ɣh
If P1 = Patm
Then P2 = Patm + ɣh
P down = Pup +ɤ h

## Slide 33: EXAMPLE 2.1
Newfound Lake, a freshwater lake near Bristol, New Hampshire, has a maximum depth of 60 m, and the mean atmospheric pressure is 91 kPa. Estimate the absolute pressure in kPa at this maximum depth.

## Slide 34: Barometer
Barometer is simplest application of the hydrostatic formula.
P2 - P1 = -ρg( z2- z1 )
Mercury barometer is a tube filled with mercury and inverted in mercury reservoir.
P2 = P1+ ρg( z2- z1 ) = P1 + ρg h
At z1 top of mercury P1 = 0 since Hg has low vapor pressure P2 = Pa at the same level
P2 = Pa = ρHg g h  h = Pa/ ρHg g
e.g Pa = 101350 Pa ɤHg = 133100N/m3
then h = 0.761 m = 761 mm
mercury is used because it is the heaviest liquid
h H2O = 101350/ɣH2O = (101350/9790) m H2O

## Slide 35: Multi layer liquids

## Slide 36: EXAMPLE 2.8 modified
A tank is filled with layered liquids; 8 ft of oil, 6 ft of water, and 4 ft of mercury. Compute pressure at middle of each layer.

## Slide 37: Manometer
Based on Pascal law two points at the same level of continuous fluid have same pressure .

## Slide 38: Manometer
Based on Pascal law two points at the same level of continuous fluid have same pressure
P2 = P3 at the same level .
P2 = PA + ϒa 1h2
And P3 = P4 +ϒb 3h4
PA + ϒ a 1h2 = P4 + ϒ b 3h4
PA = - ϒ a 1h2 + P4 + ϒ b 3h4
PA = Patm + ϒ b 3h4 - ϒ a 1h2

## Slide 39: Manometer Problems
Systematic approach .
  Start at one end and write pressure there .
  Add to this , the change in the same units from one meniscus to the next one plus if next meniscus is lower and minus if it is higher
  Continue until the end of the gauge and equate the expression to the pressure at that point .

## Slide 40: Example
Example 3 Find P1- P5 = ?
P1 + ϒa 1h2 - ϒ b 2h3 + ϒ c 3h4 + ϒ d 4h5= P5
P1 – P5 = - ϒ a 1h2 + ϒ b 2h3 - ϒ c 3h4 - ϒ d 4h5
Example 4 Re work e.g 2
P1 + ϒ a 1h2 +ϒb 2h3 + - ϒ c 4h5 = P5
P1 - P5 = - ϒ b 2h3 - ϒ a 1h2 + ϒ c 4h5

## Slide 41: Example 2.4 p.76
Pressure at B is 87 kPag estimate pressure at A?

## Slide 42: Outline
Fluids
Units & dimensions
Properties of fluids
Pressure variations
Pressure forces
Buoyancy

## Slide 43: Force on plane areas
The distributed pressure forces may be replaced by a resultant force ,FR its line of action is called pressure center .
Task to calculate resultant force magnitude and direction.
Derive formula for horizontal surfaces
Derive formula for inclined surfaces.

## Slide 44: Horizontal surfaces
df =PdA but P is constant
F = ∫df= ∫ PdA= PA
Direction normal to the surface and toward the surface .
Pressure center :
To find center of pressure (Xp, Yp) moment of distributed pressure forces equals moment of FR
For Xp take moment about the y – axis

## Slide 46: Inclined surface
Consider area element dA
dF= PdA
but P = ϒh then dF =ϒhdA but h = y sinθ then dF=ϒ y sinθdA

## Slide 47: Inclined surface
FR = ϒhc A = Pc A
Resultant hydrostatic pressure force is pressure at the centroid multiplied by area of surface.

## Slide 48: Center of pressure
Distributed pressure moment about O equals FR moment about O:

## Slide 53: Book notation
Resultant force; PCG A where PCG is the pressure at centroid
Center of pressure
Y CP is below the centroid or
Ycp = Yc -Yp
Ixx is the area moment of inertia of the plate area about its centroidal x axis
X CP is below the centroid or
Xcp = Xc -Xp
where Ixy is the product of inertia of the plate

## Slide 54: Example vertical rectangular gate
Vertical gate 1.2 x 2 m , 3m deep and ɣ= 9.79 kN/m3
FR = ϒhcA but hc = 3+0.6= 3.6 m
Pressure center
yp = yc + Ic/( yc A) = hc+ Ic/( hc A)
Ic = (1/12)[ 2*1.23]
yp = 3.6+[(1/12)*2*1.23 /3.6*2*1.2] = 3.633m
What is the force P at the top of gate required to prevent gate open around pivot A?
FR * yA = P*1.2  P = FR *(4.2-3.633)/1.2 =39.97kN

## Slide 55: Example vertical triangular gate
Vertical equal sides triangle , head at free surface .
FR =PcA= ghcA
Centroid (2/3) from top hc = (2/3)d
FR = g(2/3)d*A
A= (bd/2)
So FR = g(2/3) d (bd/2) = (g/3)bd2
yp = hp = yc +[(Ic)xx/ycA] = hc +Ic/hcA
yp = (2/3)d + [bd3 /36]/(2/3)d(bd/2)= 3d/4

## Slide 56: Example 2.5 p. 80
A 5 ft wide gate hinged at B and rest against smooth surface at A. Compute (a) the force on the gate due to seawater pressure. (b) the horizontal force P exerted by the wall at A, and (c ) the reactions at the hinge B?

## Slide 57: Example 2.5 p. 80

## Slide 59: Outline
Fluids
Units & dimensions
Properties of fluids
Pressure variations
Pressure forces
Buoyancy

## Slide 60: Buoyant Forces
Completely submerged body .
dFb = dFl –dFu
= Pl dA – Pu dA
= ϒ zl dA – ϒzu dA
dF B = = ϒ(zl – zu )dA = ϒ dVbody
* buoyant force equals weight of displaced fluid “ Archimedes Principle “
Center of buoyancy : It can be shown that
XB = (1/FB ) ∫ ϒ x (zl – zu )dA = (ϒ /FB )∫ x dV = (1/V) ∫ x dV
Which is the centroid of volume ( submerged )

## Slide 61: Buoyant Forces
Body at interface of two immiscible fluids it can be shown
FB = ϒaVa +ϒbVb
Weight of fluids being displaced by the body
See e.g 2.11 p.91

## Slide 62: Floating bodies
Weight = buoyancy
Neglect buoyance due to air

## Slide 63: Buoyant Forces
weight in fluid 1 FB1 + F1 = w
ϒ1v+F1 = w
weight in fluid 2 FB2 + F2 = w
  = ϒ 2 V +F2 = w
then V = (F1-F2 )/ (ϒ2- ϒ 1 ) ; and
w = (F1 ϒ 2 - F2 ϒ 1)/ (ϒ 2 - ϒ 1 )
also
ρ = (w/g )/v = (F1 ϒ 2 - F2 ϒ 1)/ g(F1-F2 )
S.G = (w/v ) / ϒ H2o