## Slide 1
ENCS 3310 Advanced Digital Design
Testing Digital Circuits

## Slide 2: Chip Design and Development Life Cycle

## Slide 4: Why is Design For Testability Important ?
Easier to identify the structural defects in the chip and fix design errors before the product is shipped to customers.
Make the testing process more efficient, reducing the cost and time required for testing.
This can lead to significant cost savings during the manufacturing process.
Identify any defects early in the process, allowing for faster repairs and improvements in production yield.
Accelerate the development cycle by reducing the time and effort required for testing and debugging.
Easier to diagnose and fix problems in the chip design, reducing the effort required for maintenance and updates.

## Slide 5: Testing Methods
Functional testing (Exhaustive testing)
4 bits Adder has 8 inputs
Possible combinations for input = 256 input
Test all combinations

## Slide 6: Basic testing procedure
Initialise the circuit into a known state
Apply the test inputs
Compare outputs with expectation

## Slide 7: Example
Simple example circuit
a | b | c | z
0 | 0 | 0 | 0
0 | 0 | 1 | 0
0 | 1 | 0 | 0
0 | 1 | 1 | 0
1 | 0 | 0 | 0
1 | 0 | 1 | 0
1 | 1 | 0 | 0
1 | 1 | 1 | 1
a
b
c
y
z
AND1
AND1

## Slide 8: Example
a
b
c
y
z
AND1
AND1
One of the units has a fault
Node y has been short-circuited to a voltage supply rail
This node’s value is stuck at logic 0
0
1
a | b | c | z
0 | 0 | 0 | 0
0 | 0 | 1 | 0
0 | 1 | 0 | 0
0 | 1 | 1 | 0
1 | 0 | 0 | 0
1 | 0 | 1 | 0
1 | 1 | 0 | 0
1 | 1 | 1 | 1

## Slide 9: Example
a
b
c
y
z
AND1
AND1
We cannot directly probe the node (it is inside the chip)
How do we detect this?
One of the units has a fault
Node y has been short-circuited to a voltage supply rail
This node’s value is stuck at logic 0
0
1
a | b | c | z | Faulty z
0 | 0 | 0 | 0 | 0
0 | 0 | 1 | 0 | 0
0 | 1 | 0 | 0 | 0
0 | 1 | 1 | 0 | 0
1 | 0 | 0 | 0 | 0
1 | 0 | 1 | 0 | 0
1 | 1 | 0 | 0 | 0
1 | 1 | 1 | 1 | 0

## Slide 10: Exhaustive Testing
a
b
c
y
z
AND1
AND1
Apply all possible combinations of a, b, c
These inputs are called test vectors
Compare output of unit-under-test with expectation
If we find a difference, then the unit is faulty
This circuit requires 8 test vectors
(Truth table has 23=8 rows)
0
1
a | b | c | e | Faulty z
0 | 0 | 0 | 0 | 0
0 | 0 | 1 | 0 | 0
0 | 1 | 0 | 0 | 0
0 | 1 | 1 | 0 | 0
1 | 0 | 0 | 0 | 0
1 | 0 | 1 | 0 | 0
1 | 1 | 0 | 0 | 0
1 | 1 | 1 | 1 | 0

## Slide 11: Exhaustive test of combinational logic
Generalisation:
n-input combinational system requires 2n test vectors
Example: system with 32 inputs.
  Needs 232 = 4  109 test inputs.
  Using a standard 100 MHz tester would take almost a minute for just one unit
  May not be acceptable if we have a high throughput manufacturing line
n

## Slide 12: Exhaustive test of sequential logic
If system contains state memory, things get much worse.
The sequence in which we apply the inputs becomes significant.
System with n inputs and m state flip flops
2n distinct inputs
2m distinct sequences that we can apply these inputs in
Needs 2n+m test vectors for exhaustive test.
n

## Slide 13: Exhaustive test of sequential logic
Example: system with 32 inputs, containing 32 state bits
Need 232+32 = 264 = 2x1019 test vectors
100 MHz tester requires 6,000 years for one unit

## Slide 14: Non-Exhaustive Testing (Structural )
a
b
c
y
z
AND1
AND1
0
1
a | b | c | z | Faulty z
0 | 0 | 0 | 0 | 0
0 | 0 | 1 | 0 | 0
0 | 1 | 0 | 0 | 0
0 | 1 | 1 | 0 | 0
1 | 0 | 0 | 0 | 0
1 | 0 | 1 | 0 | 0
1 | 1 | 0 | 0 | 0
1 | 1 | 1 | 1 | 0
We cannot afford to apply every possible test input
Instead we must select a few
Suppose we can use only two test inputs
Will we detect the fault?

## Slide 15: Non-Exhaustive Testing (Structural )
a
b
c
y
z
AND1
AND1
0
1
a | b | c | z | Faulty z
0 | 0 | 0 | 0 | 0
0 | 0 | 1 | 0 | 0
0 | 1 | 0 | 0 | 0
0 | 1 | 1 | 0 | 0
1 | 0 | 0 | 0 | 0
1 | 0 | 1 | 0 | 0
1 | 1 | 0 | 0 | 0
1 | 1 | 1 | 1 | 0
We cannot afford to apply every possible test input
Instead we must select a few
Suppose we can use only two test inputs.
Will we detect the fault?
This is OK
Output of faulty unit is not identical to output of good unit: Fault is detected

## Slide 16: Non-Exhaustive Testing (Structural )
a
b
c
y
z
AND1
AND1
We cannot afford to apply every possible test input
Instead we must select a few
Suppose we can use only two test inputs.
Will we detect the fault?
OK if we choose a set that includes abc=111
Otherwise fault is not detected
0
1
a | b | c | z | Faulty z
0 | 0 | 0 | 0 | 0
0 | 0 | 1 | 0 | 0
0 | 1 | 0 | 0 | 0
0 | 1 | 1 | 0 | 0
1 | 0 | 0 | 0 | 0
1 | 0 | 1 | 0 | 0
1 | 1 | 0 | 0 | 0
1 | 1 | 1 | 1 | 0
This is no good
Output of faulty unit is identical to output of good unit: Fault is missed

## Slide 17: Non-Exhaustive Test (Structural )
If we can’t use all possible test vectors, we may miss faults
The percentage of faults that is detected by a set of test vectors is the fault coverage
If we can’t use all possible test vectors, fault coverage may be less than 100%.
Some choices of test vectors will have high fault coverage
Other choices will have low fault coverage
How do we choose test vectors that maximise fault coverage? (Ideally to 100%)

## Slide 18: Testing Methods – Structural
Example : Half Adder
Exhaustive => 4 test vectors (tiny circuit)
Check if sum is stuck on Vcc, What test vectors can be used?
  We need to add test vectors that produce sum = 0
Check if sum is stuck on Gnd, What test vectors can be used?
  We need to add test vectors that produce sum =1
Test vector should produce opposite of fault value

## Slide 19: Testing Methods – Structural
Example : Half Adder
use just 2 Test Vectors
 | Group 1 | Group 2 | Group 3 | Group 1
Test Vector 1 | 0 1 | 0 0 | 0 0 | 1 0
Test Vector 2 | 1 0 | 0 1 | 1 1 | 1 1
V1 Coverage |  |  |  | 
V2 Coverage |  |  |  | 
Fault Coverage |  |  |  | 
S => gnd
C => Vcc
S => gnd
C => Vcc
2/4 = 50%
S => Vcc
C => Vcc
S => gnd
C => Vcc
3/4 = 75%
S => Vcc
C => Vcc
S => Vcc
C => gnd
3/4 = 75%
S => gnd
C => Vcc
S => Vcc
C => gnd
4/4 = 100%

## Slide 20: Fault Modeling
Stuck at 1
Stuck at 0
Bridging fault (short circuit)
Open circuit
Transition delay
Wire delay
Multiple stuck at fault

## Slide 21: Fault Model
Course focus:
  Single stuck at 0 (Sa0) == Node short circuit with gnd
  Single stuck at 1 (Sa1) == Node short circuit Vcc
  Single stuck cant still discover multiple stuck points too

## Slide 22: Path sensitization
For each node in the circuit:
  Assume the fault type (S-a-0 or S-a-1)
  Perform the the following steps:
    Backtrace phase: Send the non-fault value to the node under consideration
    Propagation phase: Steer the value of the node under consideration to one of the outputs
Only inputs nodes can be controlled
Only output nodes can be observed

## Slide 23: Example problem
a
b
c
y
z
AND1
AND1
  Backtrace: Set y to 1 (Opposite to test value) => a.b=1
    A.b=1 => a=1 b=1 => y = 1 if no fault
    y = 0 if fault
Is y s-a-0?
  Propagation: y is not observable (internal). Propagate its value to z
    C must be 1 (if c = 0, z will always be 0 so no way to test)
    Z = 1 … no fault
    Z = 0 … fault
Test Vector ‘abc’ = 1 1 1

## Slide 24: Example problem
a
b
c
y
z
AND1
AND1
  Backtrace: Set y to 0 (Opposite to test value) => a.b=0
    A.b=0 => a=1 b=0
    a=0 b=1 => y = 0 if no fault
    a=0 b=0 y = 1 if fault
Is y s-a-1?
  Propagation: y is not observable (internal). Propagate its value to z
    C must be 1 (if c = 0, z will always be 0 so no way to test)
    Z = 0 … no fault
    Z = 1 … fault
Test Vectors a b c
1 0 1
0 1 1
0 0 1

## Slide 25: Example problem
a
b
c
y
z
AND1
AND1
  Backtrace: Set a to 1 (Opposite to test value) => a=1
    a = 1 if no fault
    a = 0 if fault
Is a s-a-0?
  Propagation: a is not observable (internal gate input). Propagate its value to y and z
    b must be 1 (if b = 0, y will always be 0 so no way to test)
      y = 1 … no fault
      y = 0 … fault
    c must be 1 (if b = 0, y will always be 0 so no way to test)
      z = 1 … no fault
      z = 0 … fault
Test Vector ‘abc’ = 1 1 1

## Slide 26: Example problem
a
b
c
y
z
AND1
AND1
  Backtrace: Set a to 0 (Opposite to test value) => a=1
    a = 0 if no fault
    a = 1 if fault
Is a s-a-1?
  Propagation: a is not observable (internal gate input). Propagate its value to y and z
    b must be 1 (if b = 0, y will always be 0 so no way to test)
      y = 0 … no fault
      y = 1 … fault
    c must be 1 (if b = 0, y will always be 0 so no way to test)
      z = 0 … no fault
      z =1… fault
Test Vector ‘abc’ = 0 1 1

## Slide 27: Example problem
a
b
c
y
z
AND1
AND1
Fault | Test Vectors a b c | Fault Free z | Faulty z
A s-a-0 |  | 1 | 0
B s-a-0 |  | 1 | 0
C s-a-0 |  | 1 | 0
Y s-a-0 |  | 1 | 0
Z s-a-0 |  | 1 | 0
A s-a-1 |  | 0 | 1
B s-a-1 |  | 0 | 1
C s-a-1 |  | 0 | 1
Y s-a-1 |  | 0 | 1
Z s-a-1 |  | 0 | 1
Test Vector 1 1 1 is capable of testing 5 cases
1 1 1
1 1 1
1 1 1
1 1 1 (to get 1 on z)
1 1 1 (to get 1 on z)
0 1 1
1 0 1
1 1 0
001, 011,101
Everything except 111 result in 0
000 001 010 011 100 101 110
Essential test vectors: vectors that no other vectors can cover
Such as 111 011 101 110
Exhaustive test vectors = 8 vectors
Minimal test vectors ABC
111
011
101
110

## Slide 28: Example problem
Is Y s-a-0?
Is Y s-a-1?

## Slide 29: Example problem
Is Y s-a-0?
  Backtrace: Set y to 1 (Opposite to test value)
  Y = 1 if no fault
    ___ Y = 0 if fault
  => AB = 10
  Propagation: Y is not observable (internal gate input). Propagate its value to F
    z must be 0
    ___ ___
    => CX = 0 1 => CD = 0 0
    1 0 1 1
    1 1 1 0
_______
Test Vectors : A B C D
1 0 0 0 => F = 1 no Fault
1 0 1 0 F = 0 Faulty
1 0 1 1

## Slide 30: Example problem
Is Y s-a-1?
  Backtrace: Set y to 0 (Opposite to test value)
  __ __
    AW AB
  0 0 0 1 Y = 0 if no fault Y = 1 if fault
  0 1 0 0
  10 11
  Propagation: Y is not observable (internal gate input). Propagate its value to F z must be 0 ___ ___
  => CX = 0 1 => CD = 0 0
    1 1 1 0
    1 0 1 1
_______
Test Vectors : A B C D
0 0 0 0 => F = 0 no Fault
0 0 1 0 F = 1 Faulty
0 0 1 1
0 1 0 0
0 1 1 0
0 1 1 1
1 1 0 0
1 1 1 0
1 1 1 1

## Slide 31: D Algorithm (5 value logic)
Provide convenient treatment Sa1 and Sa0 faults
The 5 values are
  logic 0
  Logic 1
  x unknown
  Introduce 2 new logic symbols:
    D: 1 in a good circuit / 0 in a faulty circuit
    D: 0 in a good circuit / 1 in a faulty circuit
  Goal of testing is to discriminate good circuits from faulty:
  Need to make at least one output go to D or D

## Slide 32: D Algorithm (5 value logic)
Test X s-a-0
X = 1 no fault, X = 0 fault
Y = 0 no fault, Y = 1 fault
W = 1 no fault, W = 0 fault
Always propagating 2 values
Prone to mistakes
  Introduce 2 new logic symbols:
    D: 1 No Fault / 0 on Fault
    D: 0 No Fault / 1 on Fault

## Slide 33: D Algorithm (5 value logic)
1
1
1
1
D
D
D
D
D
Test X s-a-0

## Slide 34: Reasoning about s-a-0, s-a-1 faults
Introduce 2 new logic symbols:
  D: 1 in a good circuit / 0 in a faulty circuit
  D: 0 in a good circuit / 1 in a faulty circuit
Goal of testing is to discriminate good circuits from faulty:
Need to make at least one output go to D or D
a | b | c | z | Faulty z
0 | 0 | 0 | 0 | 0
0 | 0 | 1 | 0 | 0
0 | 1 | 0 | 0 | 0
0 | 1 | 1 | 0 | 0
1 | 0 | 0 | 0 | 0
1 | 0 | 1 | 0 | 0
1 | 1 | 0 | 0 | 0
1 | 1 | 1 | 1 | 0
a
b
c
y
z
AND1
AND1
0
1
D

## Slide 35: Reasoning about s-a-0, s-a-1 faults
Introduce 2 new logic symbols:
  D: 1 in a good circuit / 0 in a faulty circuit
  D: 0 in a good circuit / 1 in a faulty circuit
Goal of testing is to discriminate good circuits from faulty:
Need to make at least one output go to D or D
a
b
c
y
z
AND1
AND1
0
1
a | b | c | z
0 | 0 | 0 | 0
0 | 0 | 1 | 0
0 | 1 | 0 | 0
0 | 1 | 1 | 0
1 | 0 | 0 | 0
1 | 0 | 1 | 0
1 | 1 | 0 | 0
1 | 1 | 1 | D
Not useful to test for y s-a-0
Effective test

## Slide 36: Fault oriented testing
If we know what fault we are looking for:
We don’t need to test whole truth table
Just find one effective test
Then continue checking process for all other possible faults
a
b
c
y
z
AND1
AND1
0
1
a | b | c | z
0 | 0 | 0 | 0
0 | 0 | 1 | 0
0 | 1 | 0 | 0
0 | 1 | 1 | 0
1 | 0 | 0 | 0
1 | 0 | 1 | 0
1 | 1 | 0 | 0
1 | 1 | 1 | D
Effective test
Not useful to test for y s-a-0
abc=111 tests for y s-a-0
1
1
1
D
D

## Slide 37: Fault oriented testing
If we know what fault we are looking for
We don’t need to test whole truth table
Just find one effective test
Then continue checking process for all other possible faults
a
b
c
y
z
AND1
AND1
0
1
 | a | b | c | z
y s-a-0 | 1 | 1 | 1 | D
y s-a-1 |  |  |  | 
z s-a-0 |  |  |  | 
z s-a-1 |  |  |  | 
a s-a-0 |  |  |  | 
a s-a-1 |  |  |  | 
b s-a-0 |  |  |  | 
b s-a-1 |  |  |  | 
c s-a-0 |  |  |  | 
c s-a-1 |  |  |  | 

## Slide 38: Operations on 5 value logic
NOT Z = A
A | Z
0 | 
1 | 
X | 
D | 
D | 
1
0
X
D
D

## Slide 39: Operations on 5 value logic
AND Z = A.B
 | 0 | 1 | X | D | D
0 |  |  |  |  | 
1 |  |  |  |  | 
X |  |  |  |  | 
D |  |  |  |  | 
D |  |  |  |  | 
B
A
0
0
0
0
0
0
1
X
D
D
0
X
0
0
0
0
X
X
X
X
X
D
D
D
D

## Slide 40: Operations on 5 value logic
OR Z = A+B
 | 0 | 1 | X | D | D
0 |  |  |  |  | 
1 |  |  |  |  | 
X |  |  |  |  | 
D |  |  |  |  | 
D |  |  |  |  | 
B
A
0
1
X
D
1
1
1
1
1
D
X
X
D
1
1
1
1
X
X
X
X
1
D
D
D
Other Gates can be extracted from the basic AND OR NOT gates

## Slide 41: Example
Test B s-a-1
Can propagate B through one of 3 paths
  If one test vector is required, then any good path can result in one test vector
  If all test vectors are required, all paths should be tested
  To get the minimal set for the circuit all test vectors should be required
Check path BXWF
  Set 0 on B B = 0 No Fault and 1 Fault B = D
  A must be 1 X = D W = D
  To propagate to F, Z must be 0 Y = 1 BC = 11
  B must be 1 while initially it was set to 0 Contradiction Path Fails
Check Path BYZF Fails as it is symmetrical to path BXWF
X
Y
W
Z

## Slide 42: Example
Test B s-a-1
Check the two paths BXWF and BYZF in parallel
  Set 0 on B B = 0 No Fault and 1 Fault B = D
  BXWF: A = 1 X = D W = D
  BYZF: C = 1 Y = D Z = D
  F = D+D = D (1 no fault, 0 on fault)
  If output is in D or D Then It is a good path and good test vector
  Test Vector ABC = 101
X
Y
W
Z

## Slide 43: Example
Test B s-a-0
Check the two paths BXF and BYZF in parallel
  Set 1 on B B = 1 No Fault and 0 Fault B = D
  BXF: A = 1 X = D
  BYZF: C = 1 Y = D Z = D
  F = D+D = 1 (Output not in D or D so it can't be used for generating a test vector)
Try path BXF
  Set 1 on B B = 1 No Fault and 0 Fault B = D
  A = 1 X = D
  Z must be 0 Y = 1 BC must be 11 B MUST be 1
  B must be 1 while it was set to D D != 1 contradiction …. path fail
  Try ABC = 111 with and without B s-a-0 and notice contradiction (F will always be 1)

## Slide 44: Example
Test B s-a-0
Try path BYZF
  Set 1 on B B = 1 No Fault and 0 Fault B = D
  BYZF: C = 1 Y = D Z = D
  Need to propagate Z to F then X must be 0
  X = 0 A.B = 0 B = D A = 0
  Test vector ABC = 011
  Try this test vector with and without Bs-a-0 (not fault F=0 while on Fault F=1 F = D)

## Slide 45: Derivative
Derivative is rate of change
Rate of change of distance x with respect to time t
x
t
is big
is small
is zero
If derivative is zero, x is insensitive to t
If non-zero, then x is sensitive to t

## Slide 46: Boolean Difference
We want to know if z is sensitive to a
Boolean difference of z with respect to a is
Digital equivalent of derivative
If then z is sensitive to a
If then z is not sensitive to a
a
b
c
y
z
AND1
AND1

## Slide 47: Computation of Boolean Difference
Boolean relation between f and xi is
Work out value of this function with xi set to 1
Work out value of this function with xi set to 0
XOR the two together
This is the Boolean difference
x
1
x
2
x
3
x
n
z
XOR operator outputs a 1 when its arguments differ

## Slide 48: Computation of Boolean Difference
x
1
x
2
x
3
x
n
z
Boolean Difference and DFT
Z is sensitive to node xi when
To test xi s-a-0 :
To test xi s-a-1 :

## Slide 49: Computation of Boolean Difference

## Slide 50: Using Boolean Differences
Test for a s-a-0:
  Drive a with 1
  Make z sensitive to a, i.e. make
But
So we need to make b=1 and c=1
Is a s-a-0?
1
1
1
a
b
c
y
z
AND1
AND1

## Slide 51: Using Boolean Differences
Is a s-a-0?
1
1
1
a
b
c
y
z
AND1
AND1
a is s-a-0 when
a = 1 , b =1 , c = 1
Test Vector abc = 111
Is a s-a-0?

## Slide 52: Using Boolean Differences
Is a s-a-1?
0
1
1
a
b
c
y
z
AND1
AND1
a is s-a-1 when
a = 0 , b =1 , c = 1
Test Vector abc = 011
Is a s-a-1?

## Slide 53: Using Boolean Differences – Example 2
Test node A
Is node F sensitive to node A?
Using identity X  Y = X`.Y + X.Y`
Using De Morgan's Law
F is sensitive to A when = BC = 1
BC = 11

## Slide 54: Using Boolean Differences – Example 2
Test node A
Is node A s-a-0 ?
= 1
A. = 1
A s-a-0 when ABC = 1
ABC = 111
A s-a-0 when

## Slide 55: Using Boolean Differences – Example 2
Test node A
Is node A s-a-1 ?
= 1
A`. = 1
A s-a-0 when A`BC = 1
ABC = 011
A s-a-0 when

## Slide 56: Using Boolean Differences – Example 2
Test node B
Is node F sensitive to node B?
F is sensitive to A when = A+C` = 1
AC =
00
10
11

## Slide 57: Using Boolean Differences – Example 2
Test node B
Is node B s-a-0 ?
= 1
B. = 1
B s-a-0 when
Will be 1 when both B and (A+C`) are 1
B AC
0 0
1 0
1 1
Test Vectors:
ABC
0 1 0
1 1 0
1 1 1

## Slide 58: Using Boolean Differences – Example 2
Test node B
Is node B s-a-1 ?
= 1
B`. = 1
B s-a-0 when
Will be 1 when both B` and (A+C`) are 1
B AC
0 0 0
1 0
1 1
Test Vectors:
ABC
0 0 0
1 0 0
1 0 1

## Slide 59: Using Boolean Differences – Example 2
Test node x
Is node F sensitive to node x?
Using De Morgan's Law
F is sensitive to x when = B` + C = 1
BC =
11
01
00

## Slide 60: Using Boolean Differences – Example 2
Test node x
Is node x s-a-0 ?
= 1
x.= 1
x s-a-0 when
Test Vectors should be presented by input values not internal nodes
x=AB
x.= 1
= 1
= 1
x s-a-0 when ABC = 1
ABC = 111

## Slide 61: Using Boolean Differences – Example 2
Test node x
Is node x s-a-1 ?
= 1
x`.= 1
B s-a-0 when
Can use De Morgan's Law to simplify and get test vectors
Another option is to use the truth table to get test vectors
A | B | C | (AB)` | B`+C | 
0 | 0 | 0 |  |  | 
0 | 0 | 1 |  |  | 
0 | 1 | 0 |  |  | 
0 | 1 | 1 |  |  | 
1 | 0 | 0 |  |  | 
1 | 0 | 1 |  |  | 
1 | 1 | 0 |  |  | 
1 | 1 | 1 |  |  | 
A | B | C | (AB)` | B`+C | 
0 | 0 | 0 |  |  | 
0 | 0 | 1 |  |  | 
0 | 1 | 0 |  |  | 
0 | 1 | 1 |  |  | 
1 | 0 | 0 |  |  | 
1 | 0 | 1 |  |  | 
1 | 1 | 0 |  |  | 
1 | 1 | 1 |  |  | 
1
1
1
1
1
1
0
0
1
1
0
1
1
1
0
1
1
1
0
1
1
1
0
0
Select Test vectors where = 1
ABC
0 0 0
0 0 1
0 1 1
1 0 0
1 0 1

## Slide 62: Using Boolean Differences – Example 2
Test node y
Find Test vector to test y s-a-0 and y s-a-1

## Slide 63: Using Boolean Differences – Example 2
Test node y
Is node F sensitive to node y?
Using De Morgan's Law
F is sensitive to y when = A` + B’ = 1
AB =
00
01
10

## Slide 64: Using Boolean Differences – Example 2
Test node y
Is node y s-a-0 ?
y = 1
y.1
y s-a-0 when
Test Vectors should be presented by input values not internal nodes
y=BC’
y.= 1
= 1
= 1
y s-a-0 when A`BC` = 1
ABC = 010

## Slide 65: Using Boolean Differences – Example 2
Test node y
Is node y s-a-1 ?
y = 1
Y`.1
y s-a-0 when
Y`.1
= B` + A`C = 1
y s-a-1 when B` + A`C = 1
ABC = 000
001
100
101
011

## Slide 66: Untestable Faults
Due to existence of redundant hardware
  Completely untestable node
  Partially untestable

## Slide 67: Untestable Faults
X s-a-0 set 1 to x ab = 11 (x = D)
If c= 0 z = 0 w =0
If c =1 z = D w = D.D = 0
W is not presented as D or D, X s-a-0 is untestable
Test node x s-a-0

## Slide 68: Untestable Faults
X s-a-1 set 0 to x ab = 00 , 01, 10
If c= 0 z = 0 w =0
If c =1 z = D w = D.D = 0
W is not presented as D or D, X s-a-1 is untestable
Test node x s-a-1
Node x is completely untestable!
a | b | c | w
0 | 0 | 0 | 0
0 | 0 | 1 | 0
0 | 1 | 0 | 0
0 | 1 | 1 | 0
1 | 0 | 0 | 0
1 | 0 | 1 | 0
1 | 1 | 0 | 0
1 | 1 | 1 | 0
W is always 0
w
Redundant Hardware

## Slide 69: Untestable Faults
W = (ab)` . abz
W = (a` + b`) . abz
W = a`abz + abb`z
W = 0 + 0
W = 0
Simplify Digital Formula
Node x is completely untestable!
W is always 0
w
Redundant Hardware

## Slide 70: Partially Untestable Faults
X s-a-0 set 1 to x AB = 11 (x = D)
To propagate x to E B = 0 , Contradicts with AB = 1 x s-a-0 untestable
Test node x
X s-a-1 set 0 to x AB = 00, 10, 01 (x = D)
To propagate x to E B = 0 AB = 00, 10
Node x is partially testable …. Redundant hardware
E = AB + B
= B (A+1)
= B
Redundant Hardware
E
B

## Slide 71: Partially Untestable Faults
Test node x
Is node E sensitive to node x?
E
F is sensitive to x when = B` = 1 …… B = 0
X s-a-0 :
X.B` =1 AB.B` = 1 0 = 1 !!! Untestable
X s-a-1 :
X`.B` =1 (AB)’.B’ = 1
= (A` + B`). B` = 1
= A`B` + B` = 1
= (A` + 1). B` = 1
= B` = 1
B = 0
For X s-a-1 A is don’t care.
Can be 0 or 1
Test vector AB
0 0
1 0

## Slide 72: Fault Collapsing
Equivalent faults: Faults having exactly the same test vectors
  One test vector can cover both faults
a s-a-0 == b s-a-0 == c s-a-0
a s-a-1 == b s-a-1 == c s-a-1
ab = 00
ab = 11
x s-a-0 == y s-a-1
a s-a-0 == b s-a-0 == c s-a-1

## Slide 73: Fault Collapsing
Dominant Fault: Fault F1 is said to dominate F2 if test vectors of F2 are subset of F1 test vectors
F1 F2
abc abc
000 111
111 101
101
F1 Dominates F2
Shall we adopt F1 test vectors or F2?
F2
As any of F2 test vectors can cover F1
The opposite is not true!

## Slide 74: Fault Collapsing
Dominant Fault: Fault F1 is said to dominate F2 if test vectors of F2 are subset of F1 test vectors
a s-a-1 b s-a-1 c s-a-1
ab
01
ab
10
ab
00
01
10
Test Vectors
a s-a-0 b s-a-0 c s-a-0
ab
10
ab
01
ab
01
10
11
Test Vectors

## Slide 75: Fault Collapsing
Dominant Fault: Fault F1 is said to dominate F2 if test vectors of F2 are subset of F1 test vectors
a s-a-1 b s-a-1 c s-a-0
ab
01
ab
10
ab
00
01
10
Test Vectors
a s-a-0 b s-a-0 c s-a-1
ab
10
ab
01
ab
01
10
11
Test Vectors

## Slide 76: Fault Collapsing Example
s-a-0
s-a-1
s-a-0
s-a-1
s-a-0
s-a-1
s-a-0
s-a-1
s-a-0
s-a-1
s-a-0
s-a-1
s-a-0
s-a-1
s-a-0
s-a-1
s-a-0
s-a-1
s-a-0
s-a-1
s-a-0
s-a-1
s-a-0
s-a-1
s-a-0
s-a-1
s-a-0
s-a-1
s-a-0
s-a-1
Exhaustive Testing
8 inputs => 256 test vector
Structural (Fault Model)
15 node * 2 faults = 30 fault
Max 30 test vector
Fault Collapsing
15 test vector
s-a-0
s-a-1
What Will Happen With extra line
Exhaustive Testing
9 inputs => 512 test vector
Structural Testing
16 node * 2 faults = max 32 test vector
Fault Collapsing
16 test vector

## Slide 77: Fault Collapsing Example
Asa0
Asa1
Bsa0
Bsa1
Csa0
Csa1
Dsa0
Dsa1
Esa0
Esa1
Fsa0
Fsa1
Gsa0
Gsa1
Vsa0
Vsa1
Hsa0
Hsa1
Zsa0
Zsa1
X
X
X
X
X
X
X
X
X
X
X
X
X

## Slide 78: Fault Collapsing
IMPORTANT NOTE:
  Fault equivalency and dominance save time
  No need to recalculate faults
  Pay attention in exam to save solving time

## Slide 79: Design for Testability (DFT)
Testing is taken into account during the design phase
DFT: Adding extra logic to ease circuit testing after manufacturing
DFT enhances Construability and observability
Control
Observe

## Slide 80: Design for Testability (DFT)
Additional Input
Additional Output
Additional Input increases controllability
Additional Output increases Observability

## Slide 81: Design for Testability (DFT)
Ad-hoc Technique
  Adding minor changes into the design
  Target a specific problem
S1
S2
Inputs
outputs
Test Output
Increasing Observability for S1

## Slide 82: Design for Testability (DFT)
Ad-hoc Technique
  Adding minor changes into the design
  Target a specific problem
S1
S2
Inputs
outputs
Test Output
Test Input
Select test/normal

## Slide 83: Design for Testability (DFT)
Structured Technique
Comb Logic 1
Inputs
outputs
Comb Logic 2
Reg1
Reg2
Reg3
Example
  To get comb. Logic 2 functional reg 2 has to be programmed
  To program reg 2 comb logic 1 should be functional
Solution: Design all registers as shift registers connected to each other
Reg 2 can be programed without going through comb logic 1 (scan design)
Test Output
Test Input (Shift reg input)

## Slide 84: Built-in Self Test (BIST)
Circuit Has capability for self testing and detecting faults
Comb. Logic
R
E
G
REG
In normal mode, Registers are used normally as parallel in/out
In test mode, registers are used as test generators/test analyzer

## Slide 85: Built-in Self Test (BIST)
Test Generator: Should be able to generate large number of test vectors
Counters can be used as a test generators but with major disadvantages:
  Counters are more complicated HW than normal registers
  To covers are inputs, all bits of a counter should be triggered. For large counters (e.g 64 bit) it will be impossible to trigger MSB of the counter

## Slide 86: Linear Feedback Shift Register (LFSR)
Linear feedback shift register (LFSR) is a shift register whose input bit is the output of a linear function of two or more of its previous state
Produces a sequence of numbers. The next value of the sequence depends on the current value. The first value is usually called seed. Usually, the function XOR is used to link two consecutive values.
Seed can be any value except 0

## Slide 88: 3 bit LFSR
Seed 111
1
1
1
S0 S1 S2
Cycle S0 S1 S2
0 1 1 1
1 0 1 1
2 0 0 1
3 1 0 0
4 0 1 0
5 1 0 1
6 1 1 0
7 1 1 1
Generated all values between 1-7
No repeated value until all possible values are generated

## Slide 89: 4 bit LFSR
0
0
0
S0 S1 S2 S3
Cycle S0 S1 S2 S3
0 0 0 0 1
1 1 0 0 0
2 0 1 0 0
3 0 0 1 0
4 1 0 0 1
5 1 1 0 0
6 0 1 1 0
Generated all values between 1-5
No repeated value until all possible values are generated
1
7 1 0 1 1
8 0 1 0 1
9 1 0 1 0
10 1 1 0 1
11 1 1 1 0
12 1 1 1 1
13 0 1 1 1
14 0 0 1 1
15 0 0 0 1

## Slide 90: Single Input Signature register (SISR)
Same as LFSR with an extra xor input from the circuit under test (CUT)
CUT
S0 S1 S2

## Slide 91: Single Input Signature register (SISR)
Example
10111
0
0
0
Initial value (seed) = 000
SISR can use a seed of 0 as it has additional input
Cycle | CUT | S0 | S1 | S2
0 | 1 | 0 | 0 | 0
1 | 1 | 1 | 0 | 0
2 | 1 | 0 | 1 | 0
3 | 0 | 1 | 0 | 1
4 | 1 | 0 | 1 | 0
Signature
010

## Slide 92: Single Input Signature register (SISR)
Example
10101
0
0
0
Initial value (seed) = 000
SISR can use a seed of 0 as it has additional input
Cycle | CUT | S0 | S1 | S2
0 | 1 | 0 | 0 | 0
1 | 0 | 1 | 0 | 0
2 | 1 | 1 | 1 | 0
3 | 0 | 0 | 1 | 1
4 | 1 | 1 | 0 | 1
Value != good Signature
FAULTY Circuit
Faulty Output

## Slide 93: BIST Example
1
1
1
1
1
1
1
Seed 1111
Seed 111
F
Cycle | a1 | a0 | b1 | b0
1 | 1 | 1 | 1 | 1
2 | 0 | 1 | 1 | 1
3 | 0 | 0 | 1 | 1
4 | 0 | 0 | 0 | 1
F | S0 | S1 | S2
1 | 1 | 1 | 1
0 | 1 | 1 | 1
0 | 0 | 1 | 1
0 | 0 | 0 | 1
 | 1 | 0 | 0
Signature

## Slide 94: BIST Example
1
1
1
1
1
1
1
F
Cycle | a1 | a0 | b1 | b0
1 | 1 | 1 | 1 | 1
2 | 0 | 1 | 1 | 1
3 | 0 | 0 | 1 | 1
4 | 0 | 0 | 0 | 1
F | S0 | S1 | S2
0 | 1 | 1 | 1
0 | 0 | 1 | 1
0 | 0 | 0 | 1
0 | 1 | 0 | 0
 | 0 | 1 | 0
Bad Signature
F s-a-0

## Slide 95: Example
Equal
Logic
if a == b
out = 1
else
out = 0
S0 S1 S2
a1
a0
b1
b0

## Slide 96: Multiple Input Signature register (MISR)
S3
Parallel Loading Signature register
TPG
CUT
S2
S1
S0
D3
D2
D1
D0

## Slide 97: Built In Logic Block Observation (BILBO)
BILBO
Comb. Logic
BILBO
Comb. Logic
BILBO
Comb. Logic
BILBO
Comb. Logic
BILBO
Data In
Data Out
BILBO works as:
Parallel Load
Shift register to load/read TP
Test Pattern Generator (TPG)
Test Pattern Analyzer (TA)

## Slide 98: Built-In Logic Block Observation (BILBO)
Example: 3 bit BILBO Structure
DFF
DFF
DFF
A0
A1
A2
MUX 4x1
0
1
2
3
S0
S1
MUX 4x1
0
1
2
3
S0
S1
MUX 4x1
0
1
2
3
S0
S1
I0
I1
I2
SI
A0
A1
A2
A1
A0
A1
A2
A1
A0
I1
A1
I2
I0
S1 S0
0 0 Normal Mode
0 1 Scan mode
0 LFSR (TPG)
1 1 MISR

## Slide 99: Example
Equal
Logic
a1
a0
b1
b0
C2
C1
C0
a=b
a>b
A<b

## Slide 100: Example
a1 | a0 | b0 | b1 | a=b | a>b | a<b | C1 0 | C2 0 | C3 0 |  | a=b | a>b | a<b | C1 0 | C2 0 | C3 0
1 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 1 | 0 |  | 0 | 1 | 0 | 0 | 1 | 0
1 | 1 | 0 | 0 | 0 | 1 | 0 | 0 | 1 | 1 |  | 0 | 1 | 0 | 0 | 1 | 1
1 | 1 | 1 | 0 | 0 | 1 | 0 | 1 | 1 | 1 |  | 0 | 1 | 0 | 1 | 1 | 1
1 | 1 | 1 | 1 | 1 | 0 | 0 | 1 | 1 | 1 |  | 0 | 0 | 0 | 0 | 1 | 1
0 | 1 | 1 | 1 | 0 | 0 | 1 | 0 | 1 | 0 |  | 0 | 0 | 1 | 1 | 0 | 0
1 | 0 | 1 | 1 | 0 | 0 | 1 | 0 | 0 | 0 |  | 0 | 0 | 1 | 1 | 1 | 1
0 | 1 | 0 | 1 | 1 | 0 | 0 | 1 | 0 | 0 |  | 0 | 0 | 0 | 0 | 1 | 1
1 | 0 | 1 | 0 | 1 | 0 | 0 | 0 | 1 | 0 |  | 0 | 0 | 0 | 1 | 0 | 1
1 | 1 | 0 | 1 | 0 | 1 | 0 | 0 | 1 | 1 |  | 0 | 1 | 0 | 0 | 0 | 0
0 | 1 | 1 | 0 | 0 | 0 | 1 | 1 | 0 | 0 |  | 0 | 0 | 1 | 0 | 0 | 1
0 | 0 | 1 | 1 | 0 | 0 | 1 | 1 | 1 | 1 |  | 0 | 0 | 1 | 1 | 0 | 1
1 | 0 | 0 | 1 | 0 | 1 | 0 | 0 | 0 | 1 |  | 0 | 1 | 0 | 0 | 0 | 0
0 | 1 | 0 | 0 | 0 | 1 | 0 | 1 | 1 | 0 |  | 0 | 1 | 0 | 0 | 1 | 0
0 | 0 | 1 | 0 | 0 | 0 | 1 | 1 | 1 | 0 |  | 0 | 0 | 1 | 0 | 0 | 0
0 | 0 | 0 | 1 | 0 | 0 | 1 | 1 | 1 | 0 |  | 0 | 0 | 1 | 0 | 0 | 1
Assume a=b output signal is stuck at 0
Bad Signature
1
0
0
0
0
0
0
LFSR TPG
Output
MISR