## Slide 1: Fluid Mechanics I Chapter 1 Introduction
Dr. Afif Akel Hasan
Mechanical & Mechatronics Engineering

## Slide 2: Outline
Fluids
Units & dimensions
Properties o fluids
Viscosity

## Slide 3: Fluid
Matter consist of two states ; fluid and solid .
A solid can resist sheer stress by a static deformation . The fluid move and deforms continuously as long as sheer stress is applied.
A fluid continues to flow for as long as the force is applied and will not recover its original form when the force is removed.
Shear force : force component tangent to the surface .
Shear stress is the sheer force per unit area τ = F/area .

## Slide 4: Fluid Mechanics
Fluid Mechanics : is the study of the fluids either in motion or at rest and the effects of the fluid upon the boundaries.
Fluids: Gases and liquid.
Fluid at rest : fluid statics
Fluid in motion : fluid dynamics

## Slide 5: Fluids
Fluid of two classes: liquids and gases .
A liquid composed of relatively closed – packed molecules with strong cohesive forces ,
Gases are widely spaced molecules with negligible cohesive forces .
A gas has no definite volume

## Slide 6: Engineering Application
Examples include breathing , blood flow, heart, swimming,
Equipment: Pumps, fans, turbines
Transport: ships, cars , air planes , plane engines , jets …

## Slide 7: Dimensions and Units
Primary dimensions: from which all other dimensions can be derived : mass, length, time and temperature , for ones used in fluid mechanics see Table (1.1) P. 8 .

## Slide 8: Primary unit systems
  There are three primary unit systems in use:
    the International System of Units (SI units - kg, N, m, s, K)
    the English Engineering System of Units (commonly called English units - lbm, lbf, ft, s, R)
    the British Gravitational System of Units (BG - slug, lbf, ft, s, oR)
  Units must always have numbers associated with them.
  For example, length is a dimension, but it is measured in units of feet (ft) or meters (m).

## Slide 9: Secondary dimensions
Derived or constructed from combinations of these four primary dimensions eg .
Acceleration L/T2 = LT-2 dv/dt
Force F = m a (Newton's 2nd law)
F = M L T-2
i.e 1N = 1kg .m/s2
See table 1.2 p .9 for some secondary dimensions.

## Slide 11: Secondary dimensions

## Slide 12: Prefix of units
tera- (T-) | 1012 | 1 trillion
giga- (G-) | 109 | 1 billion
mega- (M-) | 106 | 1 million
kilo- (k-) | 103 | 1 thousand
hecto- (h-) | 102 | 1 hundred
deka- (da-)** | 10 | 1 ten
deci- (d-) | 10-1 | 1 tenth
centi- (c-) | 10-2 | 1 hundredth
milli- (m-) | 10-3 | 1 thousandth
micro- (µ-) | 10-6 | 1 millionth
nano- (n-) | 10-9 | 1 billionth

## Slide 13: EXAMPLE 1.1
A body weighs 1000 lbf when exposed to a standard earth gravity g 32.174 ft/s2.
  What is its mass in kg?
  (b) What will the weight of this body be in N if it is exposed to the moon’s standard acceleration gmoon 1.62 m/s2?
  (c) How fast will the body accelerate if a net force of 400 lbf is applied to it on the moon or on the earth?

## Slide 15: EXAMPLE 1.2
An early viscosity unit in the cgs system is the poise (abbreviated P), or g/(cm. s). The viscosity of water (fresh or salt) at 293.16 K 20°C is approximately 0.01 P. Express this value in (a) SI and (b) BG units.

## Slide 16: Thermodynamic Properties of a fluid
Most common properties
Pressure P
Density ρ
Temperature T
Others for work and energy calculations:
Internal energy u
Enthalpy h = u +P/r
Specific heat Cp , Cv
Entropy s
Viscosity µ
Thermal conductivity k
Two properties such as ( P,T) are sufficient to fix the value of all other properties for pure substances.

## Slide 17: Pressure & temperature
Pressure: pressure is the stress at a point in a static fluid, or force per unit normal area P = Fnormal / Aarea
1 atmosphere = 101300 Pa = 101.30 kPa
Temperature : a measure of the internal energy level of a fluid,
Centigrade ( Celsius) and absolute K = C +273.16 .
Degree size is the same for C and K

## Slide 18: Fluid density
Density : mass per unit volume , symbol ( ρ )
ρ = m/v [ kg/m3 ]
Density is nearly constant for liquids, while increasing proportional to pressure of gases .
Liquids are treated as incompressible fluid (density doesn’t change with changing pressure ) .
e.g water density 1000kg/m3, air density 1.2 kg/m3 at 300 K 1 atm.
Mercury 13600 kg/m3.

## Slide 19: Specific gravity
Specific gravity SG : a ratio of a fluid density to standard reference fluid.
Reference fluids: water ( for liquids ) and air for gases .
SG gas = ρ gas / ρ air = ρ gas / 1.205 kg/m3
SG liquid = ρ liquid / ρ water = ρ liquid / 998 kg/m3
e.g SG Hg = 13580 / 998 = 13.6

## Slide 20: Specific weight
Specific weight: denoted by “ ɣ “ is the weight per unit volume ɣ = ρ g
since ɣ = mg /V = ρ g .
Hence units of [ɣ ] are N / m3 or lbf/ ft3 .
e.g ɣ air = 1.205*9.8 = 11.8 N/m3 = 0.0752 lbf/ft3
  at 20 C ɣ water = 9.807 *998 = 9790 N/m3 = 62.4 lbf/ft3
To remember: ɣ air = 10 N/ m3 , ɣ water = 10kN/m3

## Slide 21: Potential and Kinetic Energy
Energy stored in a system by molecular, activity and molecular bonding forces is denoted as internal energy .
Potential energy equals the work required to move up the system mass ‘m’ from one elevation to another one against the gravity field . PE = mg ∆z
Kinetic energy equals the work required to change the speed of the ‘m’ from zero to velocity V , its value is ½mV2 .
The total storage energy per unit mass in fluid mechanics is given as e = u + ½V2 + gz

## Slide 22: State relation of gases
Pure substance for a single – phase pure substance e.g water in liquid phase . Air can be consider to be a pure substance, two properties fixes state and value of other properties V = f( T,P ).
Gases at high temperature and low pressure are treated as perfect and ideal gases intermolecular forces are negligible.
Ideal gas PV = mRT
P = (m/V ) RT = ρRT
PV = n R` T
R` = universal gas constant = 8314 m2/s2.K
R = R` /( M.wt)  for air Mwt = 28.97
e.g Rair = 287 m2/s2 .K
standard air density @ 25 C Patm = 101300Pa
ρair = P/(RT) = 10300 [N/m2 ]/ (287[m2/s2.K] * 298[k]) = 1.205 kg/m3

## Slide 23: Specific heat
for gases
Specific heat at constant volume Cv = ( du/dt )v
Specific heat at constant pressure Cp = ( dh/dt )p
Specific heat ratio K = (Cp /Cv ) > 1
For air k=1.4
For ideal gases internal energy and enthalpy are only function of temperature.
u = f(t) , h = f(t)
dh = Cpo dT  ∆h = ∫ Cpo dT
du = Cvo dT  ∆u = ∫ Cvo dT

## Slide 24: Bulk modulus
A measure of compressibility of fluids is the coefficient of the Compressibility ß .
ß = - (1/v )( dv/dp)T
Bulk modulus κ = 1/ ß = - v ( dp/dv)T
For ideal gas: show that ß =1/P

## Slide 25: Vapor pressure
It is the pressure developed above the liquid when liquid in a closed container or pressure at which liquid boils .
Vapor pressure is a function of temperature e.g for water
at 100 o C Pvapor =1 atm = 101.30kPa .
at 50 o C Pvapor = 12.350 kPa
Vapor pressure of water.

## Slide 26: Cavitation
Cavitation occurs when pressure is lower than vapor pressure at given temp ,of liquid ( liquid will flash into vapor ).
For cavitation , dimensionless parameter called cavitation number is used
Ca = (Pa - P­v )/ ½ρV2
Where : Pa = ambient pressure
Pv = vapor pressure
V = flow velocity
Critical cavitation number : value of Ca below which cavitation ( bubbles formation ) Take place in a flow.

## Slide 27: Newton law of viscosity

## Slide 28: Newton law of viscosity
Consider a flow induced between a fixed lower plate and an upper plate moving at velocity “V” as force “F: is applied to the upper plate. Plate separation “h”, area of plate “A”.
It is found F = (AV/h) or
(F/A )= (V/h )
But (F/A ) = τ = sheer stress .

## Slide 29: Newton's law of viscosity
It can be shown that (V/h) = (du / dy) = (V-0) /( h-0) = (∆u /∆y )
Where u = v at y = h
u = 0 at y = 0
For linear profile (V /h) = (∆u /∆y ) = (du /dy )
Then τ = μ (du /dy ) known as Newton's law of viscosity .
Note (du /dy ) is the rate at which one layer moves relative to the adjacent layer.
μ = viscosity
μ = signifies the resistant of the fluid to the shear stress.

## Slide 30: Shear stress
If τ vs ( du/dy ) is a straight line then the fluid is Newtonian , and the slope is μ.
Non- Newtonian fluid such as long chain hydrocarbons the τ vs ( du/dy ) is not linear.
For a linear velocity profile u(y) = a +by
from B.C.
At [ y =0 u = 0 , y = h u = v ]  u = ( v/h) y

## Slide 31: EXAMPLE 1.8
Suppose that the fluid being sheared in Fig. 1.6 is SAE 30 oil at 20°C. Compute the shear stress in the oil if V = 3 m/s and h = 2 cm.

## Slide 33: Unit of viscosity
μ = τ / (du /dy )
μ = (F/A)/(V /L ) = ( F/L2) / {(L/T)/L} but F = m a = ML/T2
[μ ] = { ML / T2L2 }/(L/T)/L = (M / T L)
or [μ ] = FT / L2
[μ ] = M / TL
SI units [μ ] =kg/m.s or N.s/m2
US or BG [μ ] =slugs/ft.s
Other units poise = dynes \cm2 1N = 105 dyne
1 N.s/m2 = kg/m.s = 10 poise
centipoise = 10-2 poise
see table 1.4 p.26 for typical values of μ more data in appendix A p.771
Kinematic viscosity ν = μ /ρ  [υ] = L2 /t ( fig .A.2 p.770) .
SI m2/s BG ft2 /s

## Slide 34: Viscosity data at 20 o C

## Slide 35: EXAMPLE 1.2
An early viscosity unit in the cgs system is the poise (abbreviated P), or g/(cm. s). The viscosity of water (fresh or salt) at 293.16 K 20°C is approximately 0.01 P. Express this value in (a) SI and (b) BG units.

## Slide 36: Temperature dependence of viscosity
Since the change in viscosity is only few percent up to 100 atm , pressure effects in viscosity is neglected .
Gas viscosity increases with temperature , power law (μ / μo ) = ( T / To ) n for air n = 0.7 and T : absolute temperature μo at reference To = 273 K .
liquid viscosity decreases with temperature and roughly exponential
μ = a e-bT
or ln (μ / μo ) = a +b (To /T) + c (To /T)2
for water a = -1.94, b = -4.80 , c = 6.74 , To = 273.K , μo = 0.001792 kg /m .s

## Slide 38
Table A.1 Viscosity and Density of Water at 1 atm
Table A.2 Viscosity and Density of
Air at 1 atm

## Slide 39
Table A.3 Properties of Common
Liquids at 1 atm and 20°C (68°F)

## Slide 40: Temperature dependence of viscosity
Resistance of a fluid to shear depends on its cohesion and its rate of molecular momentum transfer.
for liquids cohesive forces are predominant cause of viscosity , hence cohesive force decreases with increase in temperature , viscosity decreases with increasing temperature .
for gases molecular activity gives to an apparent shear stress which is more important than cohesive forces . Since molecular activity increases with temperature and consequently the gas viscosity increases with increase in temperature.

## Slide 41: Reynold number
Primary number correlating the viscous behavior of fluids, Re
Re= ρVL/μ = VL/ν
Re used to distinguish flow types laminar or smooth and rough or turbulent.

## Slide 42: Surface Tension
A liquid will form an interface with a second liquid or a gas .
Surface tension results from cohesive forces, between similar molecules , and “adhesive” force between unlike molecules .
At interface cohesive force from below ( liquid ) exceeds adhesive force ( gas/liquid ) hence resulting in surface tension .
Surface tension results in formation of liquid droplets and bubbles .
It is measured by stretching force required to form the film , surface energy per unit length .
Unit of [s] : F/L SI N/m or lbf/ft
e.g water /air s = 0.073N/m
air / mercury s = 0.48 N/m

## Slide 43: Examples of surface tension
Drops of water
Soap bubble
Insects walking on water
Needle (or paper clip) floating on water

## Slide 44: Droplet
Force of pressure inside gauge is balanced by the surface tension force .
Pig π R2 = σ (2πR) = ∆pπ R2
Where π R2 = projected surface of hemisphere
2 π R = circumference of circle
∆p = Pig = 2 σ /R

## Slide 45: Air bubble
Surface tension acts on inside and outside of the bubble wall hence
∆pπ R2 = 2(2σ π R)
∆p = 4σ /R
Pig = 4σ /R

## Slide 46: Contact angle
Surface tension occurs during a gas-liquid interface, but if that interface comes in contact with a solid surface - such as the walls of a container - the interface usually curves up or down near that surface. Such a concave or convex surface shape is known as a meniscus.

## Slide 47: Capillary Action
contact angle ϴ appears when liquid intersect
with the a solid surface .
If ϴ < 90 wetting ( wets the solid )
If ϴ > 90 Non wetting liquid .
capillary action when liquid rises or falls in capillary tubes .
it is caused by surface tension and by the relative values of adhesive ( liquid to solid ) and cohesive force ( between the liquid molecules ).

## Slide 49: Example 1.9 p 31
Surface tension force at inter-face must balance the weight of the column of liquid of height (h )
(2σ π R) cosϴ = ɣ π R2 h
then h = (2 σ cosϴ /ɤR)
h > 0 positive if ϴ < 90
h < 0 negative if ϴ > 90
a ) e.g for water – air –glass ϴ = 0 σ = 0.073 N/m
ρ = 1000kg/m3 R = 1 mm
h = 2(0.073cos ϴ / (1000*9.81*0.001) = 0.015 m = 1.5 cm .
b ) for mercury – air – glass
ϴ = 130, σ = 0.48 N/m ρ = 13600 kg /m3
R = 1 mm
h = 2*0.48 *cos130 / 13600*9.81*0.001 = -0.46

## Slide 50: Basic Flow-Analysis Techniques
There are three basic ways to attack a fluid-flow problem;
  Control-volume, or integral analysis (Chap. 3)
  Infinitesimal system, or differential analysis (Chap. 4)
  Experimental study, or dimensional analysis (Chap. 5)
The flow must satisfy the three basic laws of mechanics plus a thermodynamic state relation and associated boundary conditions.
  Conservation of mass (continuity)
  Linear momentum (Newton’s second law)
  First law of thermodynamics (conservation of energy)
  A state relation like f(p, T)
  Appropriate boundary conditions at solid surfaces, interfaces, inlets, and exits