## Slide 1: Fluid Mechanics I Chapter 6 Viscous flow in ducts
Dr. Afif Akel Hasan
Mechanical & Mechatronics Engineering

## Slide 2: Outline
Laminar and Turbulent flow
Entrance effect
Friction losses in smooth pipes
Friction losses in rough pipes
Minor losses
Energy equation for pipe flow
Pipe flow problems.

## Slide 3: laminar & turbulent flow
laminar flow : in laminar flow a well – ordered pattern prevails , where by fluid layers are assumed to slide over each other.
Reynold experiment;
  when the valve is opened slightly the dye will move through pipe intact forming a thread , in this case flow is laminar.
  when valve is progressively opened the dye assumed fluctuating motion as it flows through the pipe here transitions is taking place
  further opening of valve results in a condition where by an irregular fluctuation is developed in the flow . When the dye is completely dispersed in the pipe . This irregular flow is turbulent flow .

## Slide 4: laminar & turbulent flow
laminar flow is well – ordered flow ,
Turbulent flow is an irregular ( fluctuating ) one .
laminar flow has a constant ( well – ordered ) velocity V` .
Turbulent flow velocity is fluctuated from V to V`
Fig. 6.5 Reynolds’ sketches of pipe-flow transition: (a) low-speed, laminar flow; (b) high-speed, turbulent flow

## Slide 5: Laminar & Turbulent Flow
Fig. 6.2 Flow issuing at constant speed from a pipe: (a) high viscosity, low-Reynolds-number, laminar flow; (b) low-viscosity, high-Reynolds-number, turbulent flow.

## Slide 6: Laminar & Turbulent Flow
Re is the criteria of transition from laminar to Turbulent
Re = (ρVD/µ ) = (VD/ν ) =( Inertial force / Viscous force)
For pipe flow Recritical = 2300
200<Re <4000 transition
Re > 4000 well developed turbulent flow .

## Slide 7: EXAMPLE 6.1 P . 326
The accepted transition Reynolds number for flow in a circular pipe is Red, critical = 2300. For flow through a 5-cm-diameter pipe, at what velocity will this occur at 20°C for (a) airflow and (b) water flow?
Thus transition is specified at Vd/ν = 2300.
These are very low velocities, so most engineering air and water pipe flows are turbulent, not laminar. We might expect laminar duct flow with more viscous fluids such as lubricating oils or glycerin.

## Slide 8: Entrance effect
An internal flow is constrained by the bounding walls, and the viscous effects will grow and meet and permeate the entire flow.
Viscous boundary layers grow downstream, retarding the axial flow u(r, x) at the wall and thereby accelerating the center-core flow to maintain the incompressible continuity requirement.
At a finite distance from the entrance, the boundary layers merge and the inviscid core disappears.
The tube flow is then entirely viscous, and the axial velocity adjusts
slightly further until at x= Le it no longer changes with x and is said to be fully developed, u= u(r) only.

## Slide 9: Entrance effect
Downstream of x ≥ Le the velocity profile is constant, the wall shear is constant, and the pressure drops linearly with x, for either laminar or turbulent flow.

## Slide 10: Entrance length
Dimensional analysis shows that the Reynolds number is the only parameter affecting entrance length.
For laminar flow the accepted correlation is
In turbulent flow the boundary layers grow faster, and Le is relatively shorter, according to the approximation for smooth walls

## Slide 11: EXAMPLE 6.2
A ½ in-diameter water pipe is 60 ft long and delivers water at 5 gal/min at 20°C. What fraction of this pipe is taken up by the entrance region?
This is greater than 2300; hence the flow is fully turbulent

## Slide 12: Flow in a Circular Pipe, hf
The steady-flow energy equation for pipe section 1 to 2
But V1 = V2 then
From linear momentum
Divide by knowing Z to get
Or

## Slide 13: For laminar flow
Shear stress at wall in a pipe
for the laminar velocity profile this gives
however the average velocity is half of the maximum velocity ( V = /2)
hence going back to hf
Substitute for velocity in terms of discharge as to get
This formula is known as Hagen- Poiseuille equation and used for friction losses for laminar flow in smooth pipes.

## Slide 14: EXAMPLE 6.4
An oil with 900 kg/m3 and 0.0002 m2/s flows upward through an inclined pipe as shown in Fig. E6.4. The pressure and elevation are known at sections 1 and 2, 10 m apart. Assuming steady laminar flow, (a) verify that the flow is up, (b) compute hf between 1 and 2, and compute (c) Q, (d) V, and (e) Red. Is the flow really laminar?

## Slide 15: EXAMPLE 6.4
This is well below the transition value Red 2300, and so we are fairly certain the flow is laminar.

## Slide 16: EXAMPLE 6.5
A liquid of specific weight γ= 58 lb/ft3 flows by gravity through a 1-ft tank and a 1-ft capillary tube at a rate of 0.15 ft3/h, as shown in Fig. E6.5. Sections 1 and 2 are at atmospheric pressure. K.E correction =2. Neglecting entrance effects, compute the viscosity of the liquid.
Meanwhile P1= P2 pa, and V1= 0 in the large tank. Therefore, approximately

## Slide 17: EXAMPLE 6.5
Note that L in this formula is the pipe length of 1 ft. Finally, check the Reynolds number

## Slide 18: Viscometers
Saybolt viscometer
Viscosity in centipoise from seconds Saybot

## Slide 19: Capillary viscometer

## Slide 20: Friction losses
For smooth pipes use Hagen- Poiseuille formula if laminar flow.
For rough and turbulent use correlations based on dimensional analysis.

## Slide 21: Friction head loss
Pressure drop ∆P a long a pipe in turbulent flow depends on :
pipe diameter D , length of the pipe l , viscosity µ , velocity V , density ρ, and pipe roughness ϵ .
Dimensional analysis shows k=7-3 = 4 dimensionless groups which are;
It is known that
Hence or rewrite as;

## Slide 22: Friction head loss
Where f is known as friction factor and it is a function of Reynold number and pipe roughness. This formula is known as Darcy – Weisback formula. Friction factor is given as
)= F( Re)
Various correlations exist for friction factor including;
for smooth pipe

## Slide 23: Friction head loss
For rough pipes see equation 6.64 Page 348 and 6.49 Page 348 .
Colebrook equation
It was plotted in 1944 by Moody into what is now called the Moody chart for pipe friction
An alternate explicit formula given by Haaland

## Slide 24
Moody chart for pipe
friction with smooth and rough
walls.

## Slide 26: Table 6.1 Recommended Roughness Values for Commercial Ducts

## Slide 27: Examples Moody chart
Re = 6x104 , ϵ/d =0.0002
From chart f =0.021

## Slide 28: Examples Moody chart
Re = 550000=5.5x105 , ϵ/d =0. 002
From chart f =0.024

## Slide 29: Examples Moody chart
Re = 2000000=2x106 , smooth pipe
From chart f =0.0105

## Slide 30: Examples Moody chart
Cast iron pipe with d = 5 cm and Re=3x106
For cast iron roughness ϵ= 0.26 mm then
From chart f = 0.03

## Slide 31: EXAMPLE 6.6
Compute the loss of head and pressure drop in 200 ft of horizontal 6-in-diameter asphalted cast-iron pipe carrying water with a mean velocity of 6 ft/s.
Re = (ρVD/µ ) = (VD/ν )= 2.7x 105
ϵ/d =0.0004/(6/12) = 0.0008
ϵ /d = 0.0008, and Re 2.7x 105 approximately, f = 0.02
The pressure drop for a horizontal pipe (z1= z2) is

## Slide 32: EXAMPLE 6.6
ϵ /d = 0.0008, and Re 2.7x 105 approximately, f = 0.02

## Slide 33: EXAMPLE 6.7
Oil, with 900 kg/m3 and ν= 0.00001 m2/s, flows at 0.2 m3/s through 500 m of 200-mmdiameter cast-iron pipe. Determine (a) the head loss and (b) the pressure drop if the pipe slopes down at 10° in the flow direction.

## Slide 34: EXAMPLE 6.7
Enter the Moody chart on the right at ϵ /d= 0.0013 with Re= 128,000, f = 0.0225

## Slide 35: Minor losses
Head loss :
1) Friction losses (Major losses )
2) Minor losses : (i) entrance and exit .
(ii) enlargement and contraction .
(iii) fittings .
Minor losses : hminor = K (V2/2g) = hm
K : coefficient is given for various fitting
Total head losses are

## Slide 36: Exit and entrance
For all types of exits : inward , rounded , K = 1
Entrance losses
(i)square entrance K = 0.5
(ii)Rounded K = 0.01 –0.05 or F. White p.372 fig 6.21 (b)
(iii)Re-entrant ( inward) K = 0.8-1.0 see fig 6.24(a) P.372 “F. White “

## Slide 37: Entrance
Fig. 6.21 Entrance and exit loss coefficients:
reentrant inlets
Example: L=0.5 in and d=2 in. then L/d = 0.5/2=0.25 and K=0.9 for thin tube and 0.7 if tube is 0.05 in thick ( t/d=0.05/2=.025)

## Slide 38: Entrance
Fig. 6.21 (b) rounded and beveled inlets.
Example d=2 in, r=0.25 then r/d = 0.125 and K=0.1

## Slide 39: Sudden expansion/ Contraction
It can be shown using continuity , Bernoulli's ,and moment equations that for a sudden expansion ,
hm = KSE( V2 /2g )
where
Sudden contraction may use ,
See (fig 6.22 P.372 F. White )
Example if d=1 in and D=2 in: find KSE and KSC Then d/D=0.5 and
KSE =0.55 while KSC= 0.32

## Slide 40: Gradual expansion
Fig. 6.23 Flow losses in a gradual conical expansion region P. 373 “F. White”

## Slide 41: Gradual contraction
For a gradual contraction, the loss is very small, as seen from the following experimental values.

## Slide 42: Pipe fittings
hminor = K (V2/2g)
K depends on type of fitting, pipe diameter, type of connection.
Pipe connections : screwed or flanged
Type of fittings include; valves, elbows, tees.

## Slide 43: Valves
Globe valves
Gate valves
Non-return valves
Angle valves

## Slide 44: Disk valves

## Slide 45
Ball valve

## Slide 46: Pipe fittings

## Slide 47: Resistance Coefficients -fittings
hminor = K (V2/2g)

## Slide 48: Elbows

## Slide 49: Tees

## Slide 50: Examples
Find K for 2 inch screwed 90 regular elbow? K=0.95
Find K for 2 inch flanged 90 regular elbow? K=0.39
Find K for 4 inch gate valve fully open if flanged, if screwed?
Flanged K=0.16, screwed K=0.11

## Slide 51: Partially opened valves
Fig. 6.18b Average-loss coefficients for partially open valves

## Slide 52: Equivalent length
Minor losses expressed in terms of equivalent length Le of pipe that has the same head losses for the same flow.
f (Le /D) (V2 /2g) = K (V2 /2g)
then Le = KD/f
Le is added to pipe length in Ll = [( Le + L ) /D] (V2 /2g) f
Example if K = 20 for a pipe where f = 0.02 and D = 300 mm then
Le = (20*(0.3)/0.02) = 300 m
In general Le = (D/f) ∑Ki

## Slide 53: EXAMPLE 6.16
Water, ρ=1.94 slugs/ft3 and ν=0.000011 ft2/s, is pumped between two reservoirs at 0.2 ft3/s through 400 ft of 2-in-diameter pipe and several minor losses, as shown in Fig. E6.16. The roughness ratio is ϵ/d = 0.001. Compute the pump horsepower required.

## Slide 54: EXAMPLE 6.16

## Slide 55: Multiple pipe problems
Fig. 6.24 Examples of multiple-pipe
systems: (a) pipes in series;
(b) pipes in parallel; (c) the three-reservoir
junction problem
Single path pipe problems are covered in this course.

## Slide 56: Pipe problems
Three Types of Pipe-Flow Problems;
  Pressure drop, power unknown Type 1
  Given d, L, and V or Q,ρ ,µ , and g, compute the head loss hf (head- loss problem).
  Flow rate is unknown Type 2
Given d, L, hf ,ρ ,µ , and g, compute the velocity V or flow rate Q (flow- rate problem).
  Pipe diameter is unknown Type 3
  Given Q, L, hf , ρ ,µ and g, compute the diameter d of the pipe (sizing problem).

## Slide 57: Type 1 Pressure is unknown
Straight forward solution . Conditions at one section , l, ϵ , geometry ,flow are all given and the condition at other section is desired ( P2 or ∆P ).
See example 6.16 pump head and power are required.

## Slide 58: Pipe equations

## Slide 59: Type 2 Find the Flow Rate
Pressure ,L ,ϵ , and geometry are given.
Iterative procedure is followed using Energy equation, and Moody’s chart as follows:
  1) assume friction factor f
  2) solve energy equations for V
  3) calculate Re and find new ‘f” .
  4) compare new “f” with previous one if small difference then use this ‘f’ to find V then Q . If still large difference then go to “2” above and repeat procedure .

## Slide 60: Example : 5.13 p .240 Streeter
Water at 15 oC ( ϒ = 1.13x 10-6 m2 /s ) flows through 300 mm diameter riveted steel ϵ= 3 mm with head loss of 6 m = hloss in 300 m . Determine the flow .
(ϵ/D ) = (0.003/0.30) = 0.01
assume f 1 = 0.04
Energy equation hl= f (L/D)(V2/2g) = 6m
V=(2ghlD/Lf)0.5 , V = 1.715 m/s
Re = (ρVD/m ) = (VD/ν ) = 455000 from Moody’s chart
f2 =0.038
since |f2 – f1| = 0.002 is small enough then Q = AV = (∏/4)(0.3)2 V
Q = 0.1245 m3/s

## Slide 61: EXAMPLE 6.9
Oil, with 950 kg/m3 and ν=2 E-5 m2/s, flows through a 30-cm-diameter pipe 100 m long with a head loss of 8 m. The roughness ratio is ε/d =0.0002. Find the average velocity and flow rate.
Energy equation Steady flow same Z no change in velocity, only pressure drop due to friction.
hf =8

## Slide 64: Type 3; Diameter is Unknown
Pressure ,L,ϵ,Q and geometry are given, diameter is desired .
Follow iterative procedure
Write energy equation in terms “f” and “D”
Assumed friction factor f1 ,then solve energy equation for “first diameter D1 “
Calculate V = (Q/A ) then Re then f2 from Moody’s chart
Now find “new D2 “ from energy equation if new f is close to previous f then stop if not repeat procedure | f2 – f1 | < ∂
note : select the next largest pipe size for nominal or commercial pipe.

## Slide 65: Diameter is Unknown

## Slide 66: Example 5.14 p . 242 Streeter
Determine the size of clean wrought – iron pipe required to convey 250 liter/s oil (ν = 1x10-5 m2/s) through 3000 m with head loss hf = 25m.N/N.
hf = (l/D)f(V2/2g)
V = Q/[(π/4)D2]
hf = (f/2g)(l/D)(Q2/π)(16/D4)
D5 = (8 l Q2 / hf gπ2) f = C f
D5 = (8 * 3000 * 0.252 / 25 * 9.8 *π2) f = 0.62 f
- assume f1 = 0.02 then D1 = 0.62 * 0.02 = 0.0416 m
- Re = (VD/ν ) = (4Q/ π Dν ) =
(4 * 0.25/ π * D *10-5 ) = 31830/D = 76500
(e/D) = 0.00011 from Moody f2 = 0.0195
D2 = [0.62f]0.5 = 0.413 Re = 75700  f3 = 0.0196
| f3 – f2 | = 0.0001 then D = 0.413 m

## Slide 68: Non circular Conduits
For non circular cross section ,you may solve using all previous relation and method by replacing the diameter with hydraulic diameter.
Dh = 4 (cross section Area / wetted perimeter ) = 4A/Pw
Example:
(i) Circular Dh = 4π (D2/4)/ π D = D
(ii) Rectangular Dh = 4ba/(2b+2a) = 2 ba/(b+a)
  For two parallel sheets where length b is much larger than separation a between the sheets Dh = 2 ba/(b+a) = 2a
(iii) Circular annulus
Dh = 4[π(D12/4) - π(D22/4)]/ [π D1 + π D2] = [(D12-D22 )/(D1+D2)] = (D1-D2)

## Slide 69: hydraulic diameter
Concentric annulus
Deff/Dh= 1/ζ are given in Table 6.3
Effective diameter solution is not required only hydraulic diameter solution.

## Slide 70: EXAMPLE 6.13
Fluid flows at an average velocity of 6 ft/s between horizontal parallel plates a distance of 2.4 in apart. Find the head loss and pressure drop for each 100 ft of length for ρ= 1.9 slugs/ft3 and (a) ν=0.00002 ft3/s and (b) ν=0.002 ft3/s. Assume smooth walls.
The spacing is 2h = 2.4 in= 0.2 ft, and Dh =4h= 0.4 ft.
For reasonable accuracy, simply look on the Moody chart for smooth walls
  separation a between the sheets
  Dh = 2a

## Slide 71: EXAMPLE 6.14
What should the reservoir level h be to maintain a flow of 0.01 m3/s through the commercial steel annulus 30 m long shown in Fig. E6.14? Neglect entrance effects and take ρ=1000 kg/m3 and ν=1.02x106 m2/s for water.

## Slide 72: EXAMPLE 6.14
where 0.046 mm has been read from Table 6.1 for commercial steel surfaces. From the Moody chart, read f = 0.0232.

## Slide 73
End of pipe flow